## Slide 1: Digital Logic Design
(AMD X4 Proc; photo: Sc. Am, Jan. 2010)
Spring 2021

## Slide 2: Course Description
This course provides a modern introduction to logic design and the basic building blocks used in digital systems, in particular digital computers.
It starts with a discussion of combinational logic: logic gates, minimization techniques, arithmetic circuits, and modern logic devices such as field programmable logic gates.
The second part of the course deals with sequential circuits: flip-flops, synthesis of sequential circuits, and case studies, including counters, registers, and random access memories.
State machines will then be discussed and illustrated through case studies of more complex systems using programmable logic devices. Different representations including truth table, logic gate, timing diagram, switch representation, and state diagram will be discussed.

## Slide 3: Course Logistics
Textbook:
  "Digital Design: With an Introduction to the Verilog HDL”
  M. M. Mano, M. D. Ciletti), 5th ed., Prentice Hall.
Reference Text Book:
  "Logic and Computer Design Fundamentals," , by M. Mano and C. Kime,

## Slide 23: Digital Circuits are Everywhere
Communications
Multi-media
Manufacturing
Consumer electronics
Health care
Defense and security
Software
Automotive, etc
(Source: R. Tummala, IEEE Spectrum, June 2006)

## Slide 24: Life Changers
See artilcel at: http://knowledge.wharton.upenn.edu/article.cfm?articleid=2163
Of these 30 innovations , 10 are directly related to advances in Digital Logic and Solid State Circuits;
Another 8 are the indirect results of ICs.
Notes: Nightly business report on PBS: Top innovations of the last 30 yrs, according to judges at the Univ. of Pennsylvania’s Wharton School

## Slide 25
Deals with building blocks of digital systems
EE Times, Berkeley Design Tech.
(D. Rommel)
(Intel)
?
Notes: PCI: Peripheral Component Interconnect
ISA: Industrial Standard Architecture
EIDE (Enhanced Integrated Drive Electronics: connects that connect cables for Hard drives, Floppy drives.

## Slide 26: What are Logic Gates built from?
The transistor is the workhorse of every electronic device.
Digital building blocks
Transistor
Transistors:

## Slide 27: What is a Transistor?
Electronic, solid-state device that can amplify an electric signal:
  Vout > Vin
  Powerout > Powerin
Mike
Id
input
output
in
S
out
B
transistor
(Source: IMEC)

## Slide 28: Digital Model of a Transistor
We make abstraction of the signals: 0 or 1
As a result a transistors can be considered a switch (on or off; 1 or ;):

## Slide 29: Ten quintillion
Ten quintillion: 10x1018
  Is about the number grains of rice harvested in 2004
  Number of transistors fabricated in 2004
  In 2008: 1B transistors fabricated/capita

## Slide 30: What is an IC?
An Integrated Circuit is a miniaturized electronic circuits whose components (transistors, resistors, capacitors) are build on the surface of a semiconductor wafer, using the same planar fabrication technology.
(Source: http://www.majelac.com/images/wafer_dicing.jpg)
(Source: Wikipedia)
(Picture: Scientific American, Jan. 2010)

## Slide 31: Intel Itanium 9300 Tukwila Processor
(source: www.tgdaily.com)
Four cores
Over 2 billion transistors!

## Slide 32: Chip complexity
Compare to a street map
Complexity of the USA
Submicron and nanoscale dimensions
(AMD X4 Proc: 758 million transistors; photo: Sc. Am, Jan. 2010)

## Slide 33: World of the Small
5 layers of interconnections
(IBM Corp.)
Logic Level
Circuit Level
Chip level
(VLSI)

## Slide 34: Moore’s Law
Chip complexity doubles every two years
First 2-Billion Trans. Processor (Tukwila: Itanium processor); Production Q1, 2010

## Slide 35: 1. Number Systems

## Slide 36
Notes: https://www.sliderulemuseum.com/Abaci/THE_ABACUS_HANDBOOK.pdf

## Slide 37: Human perception
We naturally live in a base 10 environment
Computer exist in a base 2 environment
So give the computer/digital system the task of doing the conversions for us.

## Slide 38: Binary Codes
“An n-bit binary code is a group of n bits that assume up to 2n distinct combinations of 1s and 0s, with each combination representing one element of the set being coded”
For the 10 digits need a 4 bit code. One code is called Binary Coded Decimal (BCD)

## Slide 39
There are 10 kinds of people in the world:
those who understand binary numerals, and
those who don't.

## Slide 40: Decimal and BCD
The BCD is simply the 4 bit representation of the decimal digit.
For multiple digit base 10 numbers, each symbol is represented by its BCD digit
What happened to 6 digits not used?

## Slide 41: Common Number Systems
System | Base | Symbols | Used by humans? | Used in computers?
Decimal | 10 | 0, 1, … 9 | Yes | No
Binary | 2 | 0, 1 | No | Yes
Octal | 8 | 0, 1, … 7 | No | No
Hexa- decimal | 16 | 0, 1, … 9, A, B, … F | No | No

## Slide 42: Quantities/Counting (1 of 3)
Decimal | Binary | Octal | Hexa- decimal
0 | 0 | 0 | 0
1 | 1 | 1 | 1
2 | 10 | 2 | 2
3 | 11 | 3 | 3
4 | 100 | 4 | 4
5 | 101 | 5 | 5
6 | 110 | 6 | 6
7 | 111 | 7 | 7
p. 33

## Slide 43: Quantities/Counting (2 of 3)
Decimal | Binary | Octal | Hexa- decimal
8 | 1000 | 10 | 8
9 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F

## Slide 44: Quantities/Counting (3 of 3)
Decimal | Binary | Octal | Hexa- decimal
16 | 10000 | 20 | 10
17 | 10001 | 21 | 11
18 | 10010 | 22 | 12
19 | 10011 | 23 | 13
20 | 10100 | 24 | 14
21 | 10101 | 25 | 15
22 | 10110 | 26 | 16
23 | 10111 | 27 | 17
Etc.

## Slide 45: Conversion - Summary
Binary
Decimal
Hexadecimal
Octal
Divisions by 16
∑Ai.16i
∑ Ai.8i
Divisions by 8
Divisons by 2
ΣAi.2i
Group in bits of 3
Group in bits of 4
Octal ↔Hex: through the binary representation

## Slide 46: Conversion Among Bases
The possibilities:
Hexadecimal
Decimal
Octal
Binary
pp. 40-46

## Slide 47: Quick Example
2510 = 110012 = 318 = 1916
Base

## Slide 48: Decimal to Decimal (just for fun)
Hexadecimal
Decimal
Octal
Binary
Next slide…

## Slide 49
12510 => 5 x 100 = 5 2 x 101 = 20 1 x 102 = 100 125
Base
Weight

## Slide 50: Binary to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 51: Binary to Decimal
Technique
  Multiply each bit by 2n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 52: Example
1010112 => 1 x 20 = 1 1 x 21 = 2 0 x 22 = 0 1 x 23 = 8 0 x 24 = 0 1 x 25 = 32
4310
Bit “0”

## Slide 53: Octal to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 54: Octal to Decimal
Technique
  Multiply each bit by 8n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 55: Example
7248 => 4 x 80 = 4 2 x 81 = 16 7 x 82 = 448 46810

## Slide 56: Hexadecimal to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 57: Hexadecimal to Decimal
Technique
  Multiply each bit by 16n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 58: Example
ABC16 => C x 160 = 12 x 1 = 12 B x 161 = 11 x 16 = 176 A x 162 = 10 x 256 = 2560
274810

## Slide 59: Decimal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 60: Decimal to Binary
Technique
  Divide by two, keep track of the remainder
  First remainder is bit 0 (LSB, least-significant bit)
  Second remainder is bit 1
  Etc.

## Slide 61: Example
12510 = ?2
2 125 62 1
2 31 0
2 15 1
2 7 1
2 3 1
2 1 1
2 0 1
12510 = 11111012

## Slide 62: Octal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 63: Octal to Binary
Technique
  Convert each octal digit to a 3-bit equivalent binary representation

## Slide 64: Example
7058 = ?2
7 0 5
111 000 101
7058 = 1110001012

## Slide 65: Hexadecimal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 66: Hexadecimal to Binary
Technique
  Convert each hexadecimal digit to a 4-bit equivalent binary representation

## Slide 67: Example
10AF16 = ?2
1 0 A F
0001 0000 1010 1111
10AF16 = 00010000101011112

## Slide 68: Decimal to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 69: Decimal to Octal
Technique
  Divide by 8
  Keep track of the remainder

## Slide 70: Example
123410 = ?8
8 1234
154 2
8
19 2
8
2 3
8
0 2
123410 = 23228

## Slide 71: Decimal to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 72: Decimal to Hexadecimal
Technique
  Divide by 16
  Keep track of the remainder

## Slide 73: Example
123410 = ?16
123410 = 4D216
16 1234
77 2
16
4 13 = D
16
0 4

## Slide 74: Binary to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 75: Binary to Octal
Technique
  Group bits in threes, starting on right
  Convert to octal digits

## Slide 76: Example
10110101112 = ?8
1 011 010 111
1 3 2 7
10110101112 = 13278

## Slide 77: Binary to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 78: Binary to Hexadecimal
Technique
  Group bits in fours, starting on right
  Convert to hexadecimal digits

## Slide 79: Example
10101110112 = ?16
10 1011 1011
B B
10101110112 = 2BB16

## Slide 80: Octal to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 81: Octal to Hexadecimal
Technique
  Use binary as an intermediary

## Slide 82: Example
10768 = ?16
1 0 7 6
001 000 111 110
2 3 E
10768 = 23E16

## Slide 83: Hexadecimal to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 84: Hexadecimal to Octal
Technique
  Use binary as an intermediary

## Slide 85: Example
1F0C16 = ?8
1 F 0 C
0001 1111 0000 1100
1 7 4 1 4
1F0C16 = 174148

## Slide 86: Exercise – Convert ...
Don’t use a calculator!
Decimal | Binary | Octal | Hexa- decimal
33 |  |  | 
 | 1110101 |  | 
 |  | 703 | 
 |  |  | 1AF

## Slide 87: Common Powers (1 of 2)
Base 10
Power | Preface | Symbol
10-12 | pico | p
10-9 | nano | n
10-6 | micro | 
10-3 | milli | m
103 | kilo | k
106 | mega | M
109 | giga | G
1012 | tera | T
Value
.000000000001
.000000001
.000001
.001
1000
1000000
1000000000
1000000000000

## Slide 88: Common Powers (2 of 2)
Base 2
Power | Preface | Symbol
210 | kilo | k
220 | mega | M
230 | Giga | G
Value
1024
1048576
1073741824
What is the value of “k”, “M”, and “G”?
In computing, particularly w.r.t. memory, the base-2 interpretation generally applies

## Slide 89: Example
/ 230 =
In the lab… 1. Double click on My Computer 2. Right click on C: 3. Click on Properties

## Slide 90: Review – multiplying powers
For common bases, add powers
26  210 = 216 = 65,536
or…
26  210 = 64  210 = 64k
ab  ac = ab+c

## Slide 91: Binary Addition (1 of 2)
Two 1-bit values
pp. 36-38
A | B | A + B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 10
“two”

## Slide 92: Binary Addition (2 of 2)
Two n-bit values
  Add individual bits
  Propagate carries
  E.g.,
10101 21 + 11001 + 25 101110 46
1
1

## Slide 93: Multiplication (1 of 3)
Decimal (just for fun)
pp. 39
35 x 105 175 000 35 3675

## Slide 94: Multiplication (2 of 3)
Binary, two 1-bit values
A | B | A  B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 95: Multiplication (3 of 3)
Binary, two n-bit values
  As with decimal values
  E.g.,
1110 x 1011 1110 1110 0000 1110 10011010

## Slide 96: Fractions
Decimal to decimal (just for fun)
pp. 46-50
3.14 => 4 x 10-2 = 0.04 1 x 10-1 = 0.1 3 x 100 = 3 3.14

## Slide 97: Fractions
Binary to decimal
pp. 46-50
10.1011 => 1 x 2-4 = 0.0625 1 x 2-3 = 0.125 0 x 2-2 = 0.0 1 x 2-1 = 0.5 0 x 20 = 0.0 1 x 21 = 2.0 2.6875

## Slide 98: Fractions
Decimal to binary
p. 50
3.14579
.14579 x 2 0.29158 x 2 0.58316 x 2 1.16632 x 2 0.33264 x 2 0.66528 x 2 1.33056
etc.
11.001001...

## Slide 99: Exercise – Convert ...
Don’t use a calculator!
Decimal | Binary | Octal | Hexa- decimal
29.8 |  |  | 
 | 101.1101 |  | 
 |  | 3.07 | 
 |  |  | C.82
Answer

## Slide 100: Conversion - Summary
Binary
Decimal
Hexadecimal
Octal
Divisions by 16
∑Ai.16i
∑ Ai.8i
Divisions by 8
Divisons by 2
ΣAi.2i
Group in bits of 3
Group in bits of 4
Octal ↔Hex: through the binary representation

## Slide 101: Binary Arithmetic

## Slide 142: Codes

## Slide 144: BCD

## Slide 145: BCD

## Slide 146: BCD

## Slide 147: BCD

## Slide 148: BCD Addition

## Slide 149: BCD Additions

## Slide 150: Invalid Case

## Slide 151: BCD Addition Example

## Slide 152: BCD Addition Example

## Slide 153: BCD Addition Example

## Slide 154: Codes

## Slide 155: GRAY Codes

## Slide 157: Binary to Gray Code Conversion

## Slide 158
Binary to Gray Code Conversion

## Slide 159: Binary to Gray Code Conversion

## Slide 160: Binary to Gray Code Conversion

## Slide 162: ASCII

## Slide 163: ASCII

## Slide 165: ASCII