## Slide 1: Overview chapter 4
Iterative circuits
Binary adders
  Full adder
  Ripple carry
Unsigned Binary subtraction
Binary adder-subtractors
  Signed binary numbers
  Signed binary addition and subtraction
  Overflow
Binary multiplication
Other arithmetic functions
  Design by contraction

## Slide 2: 4-1 Iterative Combinational Circuits
Arithmetic functions
  Operate on binary vectors
  Use the same subfunction in each bit position
One can design a functional block for the subfunction and repeat it to obtain functional block for overall function
Iterative array - a array of interconnected cells (1-D or 2-D arrays)
Notes: So far we dealt with logic operations such as AND, OR, etc. These operations work on a bit per bit basis. E.g. A+B had the meaning A OR B
Now we are talking about arithmetic operations: addition, subtraction, multiplication. E.g. when we write A+B is Add A to B. Notice the different meaning of the “+” sign. For addition, the representation A can be a word (multi bit or a vector)
These are very important in digital systems and knowing how to implement these are essential to design any digital system.

## Slide 3: Block Diagram of a 1D Iterative Array
single cell
array
Example: n = 32
  Number of inputs = ?
  Truth table rows = ?
  Equations with up to ? input variables
  Equations with huge number of terms
  Design impractical!
Iterative array takes advantage of the regularity to make design feasible: Divide and Conquer!
Notes: Number of Inputs = 66
Truth Table Rows = 266
Equations with up to 66 variables

## Slide 4: 4-2 Binary Adders
Binary addition used frequently
Addition Development:
  Full-Adder (FA), a 3-input bit-wise addition functional block,
  Ripple Carry Adder, an iterative array to perform binary addition, and
  Carry-Look-Ahead Adder (CLA), a hierarchical structure to improve performance (check in Wikipedia).
Single bit
Vector
Improved
adder

## Slide 5: Functional Block: Half-Adder
A 2-input, 1-bit width binary adder that performs the following computations:
A half adder adds two bits to produce a two-bit sum
The sum is expressed as a sum bit , S and a carry bit, C
The half adder can be specified as a truth table for S and C 
X
0
0
1
1
+ Y
+ 0
+ 1
+ 0
+ 1
C S
0 0
0 1
0 1
1 0
X
Y
C
S
0
0
0
0
0
1
0
1
1
0
0
1
1
1
1
0

## Slide 6: Implementations: Half-Adder
The most common half adder implementation is:
Y
X
C
Y
X
S
×
=
Å
=
X
Y
C
S

## Slide 7: Logic Optimization: Full-Adder
Full-Adder Truth Table:
Full-Adder K-Map:
0
0
0
1
0
1
1
1
0
1
1
0
1
0
0
1
A
B
Ci
Co
S
0
0
0
0
0
1
0
1
0
0
1
1
1
0
0
1
0
1
1
1
0
1
1
1
1
1
1
1
1
1
1
1
Ci
A
+B
Co S
A
B
Ci
0
1
3
2
4
5
7
6
S
C
A
B
0
1
3
2
4
5
7
6
Co
Ci
B
Ci
A
B
A
Co
Ci
B
A
Ci
B
A
Ci
B
A
Ci
B
A
S
+
+
=
+
+
+
=

## Slide 8: Implementation: Full Adder
Full Adder Schematic for bit i
with
G = generate (=AB) and
P = propagate (=AB)
Ci+1 = Gi + Pi · Ci
or: Co= (G = Generate) OR (P =Propagate AND Ci = Carry In)
Ai
Bi
Ci
Ci+1
Gi
Pi
Si
Co = AB + (AB)Ci
or Ci+1 = AiBi + (AiBi )Ci
Si =(Ai Bi)Ci

## Slide 9: Binary Adders
To add multiple operands, we “bundle” logical signals together into vectors and use functional blocks that operate on the vectors
Example: 4-bit ripple carry adder: Adds input vectors A(3:0) and B(3:0) to get a sum vector S(3:0)
Note: carry out of cell i becomes carry in of cell i + 1
Description
Subscript
3 2 1 0
Name
Carry In
0 1 1 0
Ci
Augend
1 0 1 1
Ai
Addend
0 0 1 1
Bi
Sum
1 1 1 0
Si
Carry out
0 0 1 1
Ci+1

## Slide 10: 4-bit Ripple-Carry Binary Adder
A four-bit Ripple Carry Adder made from four 1-bit Full Adders:
Slow adder: many delays from input to output
FA
Ai
Bi
Ci
Si
Ci+1
Notes: Example: 1111 + 0001 = 10000

## Slide 11: Ripple Carry Adder

## Slide 12: Delay of a Full Adder
Assume that AND, OR gates have 1 gate delay and the XOR has 2 gate delays
Delay of the Sum and Carry bit:
Ai
Bi
Ci
Ci+1
Gi
Pi
Si
Ci
Bi
Ai
Si
Å
Å
=
2 delays
Ci
)
Bi
Ai
(
Bi
Ai
Ci+1
Å
+
=
2+2=4 delays
C0
)
B0
A0
(
B0
A0
C1
Å
+
=
@2
2+2=4 delays
@3
C0
B0
A0
S0
Å
Å
=

## Slide 13: Delay of the Carry
C1
)
B1
A1
(
B1
A1
C2
Å
+
=
@2
@?
@4
@?
Ai
Bi
Ci
Ci+1
Gi
Pi
Si
C2
)
B2
A2
(
B2
A2
C3
Å
+
=
@7
@2
@6
@8
C4
: delay 8+2 = 10
For n stage: delay of Cn: 2n+2 delays!
and Sn: 2n+4 (=@Cn + 2)
The bottleneck is the delay of the carry.
Notes: @5 adnd @6
Each FA adds 2 gate dealys to the carry!

## Slide 14: Delay in a Ripple-carry adder
@0
@0
@4
@4
@6
@6
@8
@8
@10
@10
Example: 32-bit Ripple-carry has a unit gate delay of 1ns.
What is the total delay of the adder?
What is the max frequency at which it can be clocked?
One problem with the addition of binary numbers is the length of time to propagate the ripple carry from the least significant bit to the most significant bit.
Example: 4-bit adder (n=4)
Notes: 32 bit means n=31; Thus delay of S31= 2xn+4=32+4=66 delays or 66 ns
Freq: 1/66ns= 15.2MHz

## Slide 15: Carry Lookahead Adder
Uses a different circuit to calculate the carry out (calculates it ahead), to speed up the overall addition
Requires more complex circuits.
Trade-off: speed vs. area (complexity, cost)

## Slide 16: CLA 4 bit

## Slide 17: CLA Cases

## Slide 18: Carry Look-Ahead Adder
Based of the analysis, we can now develop expressions for the output carry, Cout, of each full-adder stage for the 4-bit example.
Full-adder 1:
Cout1 = Cg1 + Cp1Cin1
Full-adder 2:
Cin2 = Cout1
Cout2 = Cg2 + Cp2Cin2
= Cg2 + Cp2Cout1
= Cg2 + Cp2(Cg1 + Cp1Cin1)
Cout2 = Cg2 + Cp2Cg1+ Cp2Cp1Cin1

## Slide 19: Carry Look-Ahead Adder
Full-adder 3:
Cin3 = Cout2
Cout3 = Cg3 + Cp3Cin3
= Cg3 + Cp3Cout2
= Cg3 + Cp3 (Cg2 +Cp2Cg1+Cp2Cp1Cin1)
Cout3 = Cg3 + Cp3Cg2 + Cp3Cp2Cg1+Cp3Cp2Cp1Cin1
Full-adder 4:
Cin4 = Cout3
Cout4 = Cg4 + Cp4Cin4
= Cg4 + Cp4Cout3
= Cg4 + Cp4(Cg3 + Cp3Cg2+Cp3Cp2Cg1+Cp3Cp2Cp1Cin1)
Cout4 = Cg4 + Cp4Cg3+Cp4Cp3Cg2+Cp4Cp3Cp2Cg1+Cp4Cp3Cp2Cp1Cin1

## Slide 20: Carry Look-Ahead Adder
Notice that in each of these expressions, the output carry for each full-adder stage is dependent only on the initial input carry (Cin1), the Cg and Cp functions of that stage, and the Cg and Cp functions of preceding stages.
Since each of the Cg and Cp functions can be expressed in terms of the A and B inputs to the full-adders.
All the output carries are immediately available (except for gate delays) and you do not have to wait for a carry to ripple though all the stages before a final result is achieved.

## Slide 21
4-bit Implementation
@4
@6
@6
@6
PFA generates G and P
C2= G1 + P1G0 + P1P0 C0
@4
C3= G2 + P2G1 + P2P1G0 + P2P1P0 C0

## Slide 22
4-bit Implementation
@4
@6
@6
@6
PFA generates G and P
C1 = G0 + P0 C0
C2= G1 + P1G0 + P1P0 C0
@4
@4
@4
Carry lookahead logic
C3= G2 + P2G1 + P2P1G0 + P2P1P0 C0

## Slide 23: a. Unsigned Subtraction
Examples:
1001 - 0111
M 9
-N 7
2
M
-N
Result
4
7
13!
Wrong answer!
0100 - 0111
Minuend
Subtrahend
borrow
0
1
4-bit numbers
0010
1101

## Slide 24: Unsigned Subtraction (cont)
What happened with the previous example:
We had to borrow a “1” which corresponds to 24.
Thus we actually added 24 or 2n:
To get the correct answer we need to subtract the previous answer from 2n:
(N-M is magnitude) plus add the (-) minus sign:
1 0100 - 0111 1101
10000 24 - 1101
(-)0011 = (-)3
M-N+2n.
2n – (M-N+2n) = N-M

## Slide 25: Unsigned Subtraction: Algorithm
Algorithm:
  Subtract the subtrahend N from the minuend M (M-N)
  If no end borrow occurs, then M > N, and the result is a non-negative number and correct.
  If an end borrow occurs, the M < N and the difference M - N + 2n is subtracted from 2n, and a minus sign is appended to the result:
Examples:
0 1000 - 0101 0011
M 8
-N 5
3
5
8
13!
16
-13
3
24
2’s complement
1 0101 - 1000 1101
correct
answer
End borrow: needs correction
10000 - 1101
(-)0011
2n -(M - N + 2n )= N-M

## Slide 26: Unsigned Adder – Subtractor
To do both unsigned addition and unsigned subtraction requires:
  Complex circuits!
   Introduce complements as an approach to simplify the circuit (see next)
B

## Slide 27: 4-3 b. Complements
Two type of complements:
  Diminished Radix Complement of N
    Defined as (rn - 1) – N, with n = number of digits or bits
    1’s complement for radix 2
  Radix Complement
    Defined as rn - N
    2’s complement in binary
As we will see shortly, subtraction is done by adding the complement of the subtrahend
If the result is negative, takes its 2’s complement

## Slide 28: Binary 1's Complement
For r = 2, N = 0111 00112, n = 8 (8 digits):
(rn – 1) = 256 -1 = 25510 or 111111112
The 1's complement of 011100112 is then:
11111111
– 01110011
10001100
Since the 2n – 1 factor consists of all 1's and since 1 – 0 = 1 and 1 – 1 = 0, the one's complement is obtained by complementing each individual bit (bitwise NOT).
rn – 1
- N
1’s compl

## Slide 29: Binary 2's Complement
For r = 2, N = 0111 00112, n = 8 (8 digits), we have:
(rn ) = 25610 or 1000000002
The 2's complement of 01110011 is then:
100000000 – 01110011 10001101
Note the result is the 1's complement plus 1:
01110011
10001100
+ 1
10001101
Invert bit-wise
2’s complement
rn
- N
2’s compl

## Slide 30: Alternate 2’s Complement Method
Given: an n-bit binary number, beginning at the least significant bit and proceeding upward:
  Copy all least significant 0’s
  Copy the first 1
  Complement all bits thereafter.
2’s Complement Example:
  10010100
  Copy underlined bits:
  100
  and complement bits to the left:
  01101100

## Slide 31: 3-3c. Subtraction with 2’s Complement
For n-digit, unsigned numbers M and N, find M  N in base 2: Algorithm
Add the 2's complement of the subtrahend N to the minuend M:
M + (2n  N) = M  N + 2n

## Slide 32: 3-3c. Subtraction with 2’s Complement
Thus one calculates M + (2n  N) = M  N + 2n
Two possibilities:
If M  N, the sum produces end carry rn which is discarded; from above, M - N remains, which is the correct answer.
If M < N, the sum does not produce an end carry and, from above, is equal to
  M  N + 2n can we rewritten as 2n  ( N  M ), which is 2's complement of ( N  M ).
  Thus, to obtain the result  (N – M) , take the 2's complement of the sum and place a  to its left:
    2n  [2n  ( N  M )] = N-M and place a minus sign in front: - (N-M)

## Slide 33: Unsigned 2’s Complement Subtraction Example 1
Find 010101002 – 010000112
01010100 01010100
–01000011 + 10111101
00010001
2’s comp
1
Discard carry
84
-67
17
The carry of 1 indicates that no correction of the result is required

## Slide 34: Unsigned 2’s Complement Subtraction Example 2
Find 010000112 – 010101002
01000011 01000011
– 01010100 + 10101100
11101111
00010001
The carry of 0 indicates that a correction of the result is required.
Result = – (00010001)
0
2’s comp
67
-84
-17
2’s comp

## Slide 35: Exercise
Do the following subtraction of the following unsigned numbers, using the 2’s complement method:
100011 – 10001
100011 - 110110
Notes: 1) 35-17 = 18
2) 35-54 = -19

## Slide 36: Example
35
-17
18
100011
- 10001
+101111
100011
100011
- 010001
010010
1
carry out
2’s compl.

## Slide 37: 4-4 Binary Adder-Subtractors
Using 2’s complement, the subtraction becomes an ADDITION.
This leads to much simpler circuit than the previous one where we needed both an ADDER and SUBTRACTOR with selective 2’s complementer and multiplexer

## Slide 38: 4-4 Binary Adder-Subtractors
Using 2’s complement, the subtraction becomes an ADDITION.
This leads to much simpler circuit than the previous one where we needed both an ADDER and SUBTRACTOR with selective 2’s complementer and multiplexer

## Slide 39: 2’s Complement Adder/Subtractor
Subtraction can be done by addition of the 2's Complement.
1. Complement each bit (1's Complement.)
2. Add 1 to the result.
The circuit shown computes A + B and A – B:
For S = 1, subtract, the 2’s complement of B is formed by using XORs to form the 1’s comp and adding the 1 applied to C0.
For S = 0, add, B is passed through unchanged

## Slide 43: Signed Binary Numbers
So far we focused on the addition and subtraction of unsigned numbers.
For SIGNED numbers:
  How to represent a sign (+ or –)?
    One need one more bit of information.
    Two ways:
      Sign + magnitude
      Signed-Complements
Thus:
  Positive number are unchanged
  Negative numbers: use one of the above methods

## Slide 44: Signed 2’s complement system
Positive numbers are unchanged
Negative numbers: take 2’s complement
Example for 4-bit word:
0 0000
+1 0001
+2 0010
+3 0011
+4 0100
+5 0101
+6 0110
+7 0111
-1 1111
-2 1110
-3 1101
-4 1100
-5 1011
-6 1010
-7 1001
-8 1000
0 indicates positive and 1 negative numbers
7 positive numbers and 8 negative ones
Notes: Notice that for negative numbers, e.g. 1101 = -3= -8 + 5

## Slide 45: 2’s Complement Arithmetic
Addition: Simple rule
  Represent negative number by its 2’s complement. Then, add the numbers including the sign bits, discarding a carry out of the sign bits (2's complement):
  Indeed, e.x. M+(-N)  M + (2n-N)
    If M ≥ N: (M-N) + 2n ignore carry out: M-N is the answer in two’s complement)
    If M ≤ N: (M-N) + 2n = 2n – (N-M) which is 2’s complement of the (negative) number (M-N): -(N-M).
Subtraction: M-N  M + (2n-N)
  Form the complement of the number you are subtracting and follow the rules for addition.

## Slide 46: Signed 2’s Complement Examples
Example 1: 1101 + 0011
Example 2: 1101 - 0011
Example 3: (5 – 11)10 (using 2’s compl.)
Notes: Example 1: -3 + 3=0. Result is 0000. The carry out of the MSB is discarded.
Example 2: -3 -3=-6; Complement 0011 to 1101 and add. Result is 1010. The carry out of the MSB is discarded.
Example 3: 5-11: 00101; takes 2’s complement of 11 (01011) = 10101; add 00101+10101= 11010 (Result) which is equal to -6

## Slide 48: Overflow Detection
Overflow occurs if n + 1 bits are required to contain the result from an n-bit addition or subtraction.
In computers there is a fixed no. of bits (e.g. n bits)
Overflow can occur for:
  Addition of two operands with the same sign
  Subtraction of operands with different signs
For a n-bit signed number the max numbers are:
  Min-Max positive no:0 to (2n-1 – 1)
  Most negative no: -2n-1 to -1
  Example of 6-bit signed no: Max Pos no is 25-1 or 31; Most negative no. is -25=-32
If the result of the addition or subtraction is outside this range, overflow will occur. Example of 6-bit numbers:
  18+15=33, or -17-21=-38 (<-32)
  No overflow in cases: 18-15, or 17-21 (within the range).

## Slide 49: Overflow examples (continued)
18
+15
33
0 1 1 1 1 0
0 1 0 0 1 0
+0 0 1 1 1 1
1 0 0 0 0 1
wrong answer
due to overflow
-31!
carries
18
- 15
3
1 1 0 0 0 0
0 1 0 0 1 0
+1 1 0 0 0 1
0 0 0 0 1 1
3
correct answer
no overflow
Overflow occurs when the carry-in into the sign bit (most left bit) is different from the carry-out of the sign bit.

## Slide 50: Overflow Detection
Simplest way to implement overflow V = Cn  Cn - 1
0 1 1 1 1 0
0 1 0 0 1 0
+0 0 1 1 1 1
1 0 0 0 0 1
Cn Cn-1

## Slide 51: Binary Multipliers
Look at combinational circuit to do this

## Slide 52: Combinational Multiplier
AND computes A0 B0
Half adder computes sum. Will need FA for larger multiplier.

## Slide 53: Larger Multiplier

## Slide 54: Exercise
Perform the following operations. The binary numbers have a sign in the left most bit and if negative they in in 2’s complement.
Indicate if overflow occurs
100111+111001
110001-010010

## Slide 55: 4-5 Other Arithmetic Functions
Convenient to design the functional blocks by contraction - removal of redundancy from circuit to which input fixing has been applied
Functions
  Incrementing and Decrementing
  Multiplication by Constant
  Division by Constant
  Zero Fill and Extension
  Multiplication

## Slide 56: Design by Contraction
Contraction is a technique for simplifying the logic in a functional block to implement a different function
  The new function must be realizable from the original function by applying rudimentary functions to its inputs
  Contraction is treated here only for application of 0s and 1s (not for X and X)
  After application of 0s and 1s, equations or the logic diagram are simplified.

## Slide 57: Incrementing & Decrementing
Incrementing
  Adding a fixed value to an arithmetic variable
  Fixed value is often 1, called counting (up)
  Examples: A + 1, B + 4
  Functional block is called incrementer
Decrementing
  Subtracting a fixed value from an arithmetic variable
  Fixed value is often 1, called counting (down)
  Examples: A - 1, B - 4
  Functional block is called decrementer

## Slide 58: Multiplication/Division by 2n
(a) Multiplication by 4=(100)2
  Shift left by 2
(b) Division by 4=(100)2
  Shift right by 2
  Remainder preserved
B
0
B
1
B
2
B
3
C
0
C
1
0
0
C
2
C
3
C
4
C
5
B
0
B
1
B
2
B
3
C
0
C
2
1
C
2
2
C
1
C
2
0
0
C
3
Example:
Multiply M=10001 (17) by 2 (10)2:
Divide M by 2:
10001
100010
Shift one bit to the left and add 0 to the right
= 34
10001
01000.1
Shift one bit to the right and add 0 on the left
=8.5