## Slide 1
Chapter 2
Combinational Logic Circuits
Binary Logic and Gates
Boolean Algebra
A
F
B

## Slide 2: Please Read Ch-2 From Book

## Slide 3: Overview Chapter 2
  Binary Logic and Gates
  Boolean Algebra
  Standard Forms
  Two-Level Optimization
  Map Manipulation
  Other Gate Types
  Exclusive-OR Operator and Gates
  High-Impedance Outputs
Notes: In this chapter we will introduce logic gates which are the simplest logic elements. However, they form the foundation of more complex blocks which will be discussed in later chapters.
We will also discuss the mathematical tools that are required to design, analyze and simplify logic function (Boolean Algebra): optimization techniques

## Slide 4: 2-1 Binary Logic and Gates
Binary logic deals with binary variables (i.e. can have two values, “0” and “1”)
Binary variables can undergo three basic logical operators AND, OR and NOT:
  AND is denoted by a dot (·)
  OR is denoted by a plus (+).
  NOT is denoted by an overbar ( ¯ ), a single quote mark (') after the variable.

## Slide 5: Operator Definitions and Truth Tables
Truth table - a tabular listing of the values of a function for all possible combinations of values on its arguments
Example: Truth tables for the basic logic operations:
1
1
1
0
0
1
0
1
0
0
0
0
Z = X·Y
Y
X
AND
OR |  | 
X | Y | Z = X+Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
0
1
1
0
X
NOT
X
Z
=

## Slide 6: Boolean Operator Precedence
The order of evaluation in a Boolean expression is:
1.
Parentheses
2.
NOT
3.
AND
4.
OR
Consequence: Parentheses appear around OR expressions
Example: F = A(B + C)(C + D)

## Slide 7: Logic Gates
In the earliest computers, switches were opened and closed by magnetic fields produced by energizing coils in relays. The switches in turn opened and closed the current paths.
Later, vacuum tubes that open and close current paths electronically replaced relays.
Today, transistors are used as electronic switches that open and close current paths.

## Slide 8: Logic Gate Symbols and Behavior
Logic gates have special symbols:
And waveform behavior in time as follows:

## Slide 9: Gate Delay
In actual physical gates, if one or more input changes causes the output to change, the output change does not occur instantaneously.
The delay between an input change(s) and the resulting output change is the gate delay denoted by tG:
tG
0
Input
1
tG
Output
Time (ns)
0
1
0
0.5
1
1.5
tG = 0.3 ns

## Slide 10: Logic Diagrams and Expressions
Example: Alarm system for a dorm room
“The alarm should go off when the door opens OR when the door is closed AND the motion detector goes off.
Inputs: “A” door A=1 (open door), B=0 (closed)
“B” motion detector, B=1 (motion detected)
Output: F
Logic Diagram
F = A + A.B
A
F
B

## Slide 11: 2-2 Boolean Algebra
George Boole,
Mathematician (self-taught),
Professor of Mathematics of then Queen's College, Cork in Ireland)
(Encycl. Brittannica online: http://www.britannica.com/)

## Slide 12: 2-2 Boolean Algebra
3.
9.
4.
2.
X
. 1
X
=
X
. 0
0
=
Boolean algebra deals with binary variables and a set of three basic logic operations: AND (.), OR (+) and NOT ( ) that satisfy basic identities
1.
X
+ 0
X
=
+
X
1
1
=
7.
8.
0
=
X . X
1
=
X + X
X = X
Existence 0 and 1 or
operations with 0 and 1
Idempotence
Involution
5.
6.
X . X
X
=
X + X
X
=
Existence complements
Basic identities
Dual
Replace “+” by “.”, “.” by +,
“0” by “1” and “1’’ by”0”
Notes: Boolean algebra deals with binary variables and a set of three basic logic operations: AND, OR and NOT which satisify a set of basic identities

## Slide 13: Boolean Algebra
Commutative
Associative
Distributive
DeMorgan’s
10.
X + Y
Y + X
=
12.
(X + Y)
Z
+
X + (Y
Z)
+
=
16.
X + Y
X . Y
=
11.
XY
YX
=
13.
(XY)
Z
X(Y
Z )
=
15.
X
+ YZ
(X + Y)
(X + Z)
=
17.
X . Y
X + Y
=
Dual
Boolean Theorems of multiple variables
14.
X (Y+
Z)
XY
XZ
+
=
Notes: Boolean algebra deals with binary variables and a set of three basic logic operations: AND, OR and NOT which satisify a set of basic identities

## Slide 14: Example: Boolean Algebraic Proof
A + A·B = A (Absorption Theorem)
Proof Steps Justification (identity or theorem)
A + A·B
= A · 1 + A · B (Operation with 1)
= A · ( 1 + B) (Distributive Law)
= A · 1 (Operation with 1)
= A

## Slide 15: Exercise
Simplify Y+X’Z+XY’ or B+A’C+AB’ using Boolean algebra
Y+X’Z+XY’
= Y+XY’+X’Z
=(Y+X)(Y+Y’) + X’Z
=(Y+X).1 + X’Z
= Y+X+X’Z
=Y+(X+X’)(X+Z)
=Y+1.(X+Z) = X+Y+Z
(COMMUTATIVE Property)
(Distributive)
(Existence compl.)
(0peration with 1)
(Distributive)
(Existence compl.)
(Operation with 1)
Justification
X+Y+Z =A + B +C

## Slide 16: Complementing Functions
Use DeMorgan's Theorem to complement a function:
  1. Interchange AND and OR operators
  Complement each constant value and literal
Notes: F = (x + y’ + z)(‘x + y + z)

## Slide 17: Example: DeMorgan’s theorem
F = AB + C (E+D)
Find F
F = AB + C (E+D)
F = AB . C (E+D)
F = (A+B) .(C + (E+D))
F = (A+B) .(C + E.D)
Exercise: find G
G = UX(Y+VZ)
Answer:
= U’+X’ + Y’V’+Y’Z’
G
Notes: Answer: G’ = (UX)’ + (Y+VZ)’
= U’+X’ + Y’(V’+Z’)
= U’+X’ + Y’V’+Y’Z’

## Slide 18: Exercise
Example: Complement G = (a + bc)d + e
G =
Notes: G' = ((a (b' + c'))+ d ) e' = (a (b' + c') + d) e'

## Slide 19: Other useful Theorems
Minimization
Absorption
Simplification
Consensus
XY + XY = Y
(X + Y)(X + Y) = Y
X + XY = X
X(X + Y) = X
X + XY = X + Y
X(X + Y) = XY
XY + XZ + YZ = XY + XZ
(X + Y)( X + Z)(Y + Z) = (X + Y)( X + Z)
Dual
Notes: Consensus:
xy + x’z + yz = xy + x’z + yz( x+x’)
= xy(1+z) + x’z(1+y)
= xy + x’z

## Slide 20: Proof the Consensus Theorem
AB + AC + BC = AB + AC (Consensus Theorem)
Proof Steps Justification (identity or theorem)
AB + AC + BC
= AB + AC + 1 · BC operation 1
= AB +AC + (A + A) · BC existence
=
AB + AC + ABC + ABC distributive
= AB + ABC + AC + ABC commutative
= AB(1+C) + AC(1+B) distributive
= AB.1 + AC.1 operation with 1
= AB + AC operation with 1
Notes: Justification 1: 1 . X = X
Justification 2: X + X’ = 1
= AB + A’C + ABC + A’BC X(Y + Z) = XY + XZ (Distributive Law)
= AB + ABC + A’C + A’BC X + Y = Y + X (Commutative Law)
= AB . 1 + ABC + A’C . 1 + A’C . B X . 1 = X, X . Y = Y . X (Commutative Law)
= AB (1 + C) + A’C (1 + B) X(Y + Z) = XY +XZ (Distributive Law)
= AB . 1 + A’C . 1 = AB + A’C X . 1 = X

## Slide 21: General Strategies
Use idempotency to eliminate terms:
Complimentarily or existence complements:
Absorption:
Adsorption:
DeMorgan:
Consensus:
X . X
X
=
X + X
X
=
0
=
X . X
1
=
X + X
X + XY = X
X(X + Y) = X
X + XY = X + Y
X(X + Y) = XY
XY + XZ + YZ = XY + XZ
(X + Y)( X + Z)(Y + Z) = (X + Y)( X + Z)
X + Y
X . Y
=
X . Y
X + Y
=

## Slide 22: 2-3 Standard (Canonical) Forms
It is useful to specify Boolean functions in a form that:
  Allows comparison for equality.
  Has a correspondence to the truth tables
Canonical Forms in common usage:
  Sum of Products (SOP), also called Sum or Minterms (SOM)
  Product of Sum (POS), also called Product of Maxterms (POM)

## Slide 23: Minterms
Minterms are AND terms with every variable present in either true or complemented form.
Example: Two variables (X and Y)produce 2 x 2 = 4 minterms:
Given that each binary variable may appear normal (e.g., x) or complemented (e.g., ), there are 2n minterms for n variables.
Y
X
X Y
Y
X
Y
X
x

## Slide 24: Maxterms
Maxterms are OR terms with every variable in true or complemented form.
There are 2n maxterms for n variables.
Example: Two variables (X and Y) produce 2 x 2 = 4 combinations:
Y
X
+
Y
X
+
Y
X
+
Y
X
+

## Slide 25: Maxterms and Minterms
Examples: Two variable minterms and maxterms.
The index above is important for describing which variables in the terms are true and which are complemented.
Index | Minterm | Maxterm
0 (00) | x y | x + y
1 (01) | x y | x + y
2 (10) | x y | x + y
3 (11) | x y | x + y

## Slide 26: Purpose of the Index
For Minterms:
  “1” in the index means the variable is “Not Complemented” and
  “0” means the variable is “Complemented”.
For Maxterms:
  “0” means the variable is “Not Complemented” and
  “1” means the variable is “Complemented”.

## Slide 27: Index Examples – Four Variables
Index Binary Minterm Maxterm
i Pattern mi Mi
0 0000
1 0001
3 0011
5 0101
7 0111
10 1010
13 1101
15 1111
?
?
d
c
b
a
+
+
+
d
c
b
a
d
c
b
a
d
c
b
a
+
+
+
d
c
b
a
+
+
+
d
c
b
a
d
c
b
a
+
+
+
?
d
b
a
d
c
b
a
+
+
+
?
c
i
m
M
=
i
i
i
M
m
=
Notice: the variables are in alphabetical order in a standard form
d
c
b
a
Relationship between min and MAX term?
Notes: M1 = a + b + c + d’
m3 = a’ b’ c d
m7 = a’ b c d
M 13 = a’ + b’ + c + d’

## Slide 28: Implementation of a function with minterms
x y z
index
F1
0 0 0
0
0
0 0 1
1
1
0 1 0
2
0
0 1 1
3
0
1 0 0
4
1
1 0 1
5
0
1 1 0
6
0
1 1 1
7
1
Function F1(x,y,z) defined by its truth table:
Thus F1 = m1 + m4 + m7
F1 = x’ y’ z + x y’ z’ + x y z
Short hand notation: F1 =m (1,4,7)
also called, little m notation

## Slide 29: Minterm Function Example
F(A, B, C, D, E) = m2 + m9 + m17 + m23
F(A, B, C, D, E) write in standard form:
Sum of Product (SOP) expression:
  F = Σm(2, 9, 17, 23)
A’B’C’DE’ + A’BC’D’E + AB’C’D’E + AB’CDE
m2
m9
m17
m23
Notes: F(A,B,C,D,E) = A’B’C’DE’ + A’BC’D’E + AB’C’D’E + AB’CDE

## Slide 30: Converting a function into a SOP form: F(A,B,C) = A+B’C
Write the function as a canonical SOP (with minterms)
There are three variables, A, B, and C which we take to be the standard order.
To add the missing variables:
  “ANDing” any term that has a missing variable with a term 1=( X + X’).
F=A+B’C = A(B+B’)(C+C’) + B’C(A+A’)
= ABC + ABC’ + AB’C + AB’C’ + AB’C + A’B’C
= ABC + ABC’ + AB’C + AB’C’ + A’B’C
= m7 + m6 + m5 + m4 + m1
= m1 + m4 + m5 + m6 + m7
Notes: F = A(B + B’)(C + C’) + (A + A’) B’ C
= ABC + ABC’ + AB’C + AB’C’ + AB’C + A’B’C
= ABC + ABC’ + AB’C + AB’C’ + A’B’C
= m7 + m6 + m5 + m4 + m1 = m1 + m4 + m5 + m6 + m7

## Slide 31: Expressing a function with Maxterms
Start with the SOP: F1(x,y,z) =m1 + m4 + m7
Thus its complement F1can be written as
  F1 = m0 +m2 +m3 + m5 + m6 (missing term of F1)
Apply deMorgan’s theorem on F1:
  (F1 = (m0 +m2 +m3 + m5 + m6)
  = m0.m2.m3.m5.m6
  = M0.M2.M3.M5.M6
  = ΠM(0,2,3,5,6)
  Thus the Product of Sum terms (POS):
)
z
y
z)·(x
y
·(x
z)
y
(x
F
1
+
+
+
+
+
+
=
z)
y
x
)·(
z
y
x
·(
+
+
+
+
also called, Big M notation

## Slide 32: Canonical Product of Maxterms
Any Boolean Function can be expressed as a Product of Sums (POS) or of Maxterms (POM).
  For an expression, apply the second distributive law , then “ORing” terms missing variable x with a term equal to 0=(x.x’) and then applying the distributive law again.
F= A+B’+CC’
= (A+B’+C)(A+B’+C’)
= M2.M3
  Apply the distributive law:
  Add missing variable C:
F(A,B,C)= A+A’B’
F= A+A’B’ = (A+A’)(A+B’)
= 1.(A+B’)

## Slide 33: Alternatively: use Truth Table
  For the function table, the maxterms used are the terms corresponding to the 0's.
F(A,B,C)= A+A’B’
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
1
1
0
0
1
1
1
1
M2
M3
F = M2.M3
= (A+B’+C)(A+B’+C’)
A B C F

## Slide 34: Function Complements
The complement of a function expressed as a sum of minterms is constructed by selecting the minterms missing in the sum-of-product canonical forms.
Alternatively, the complement of a function expressed by a Sum of Products form is simply the Product of Sums with the same indices.
Example: Given
)
7
,
5
,
3
,
1
(
)
z
,
y
,
x
(
F
m
S
=
)
6
,
4
,
2
,
0
(
)
z
,
y
,
x
(
F
m
S
=
)
7
,
5
,
3
,
1
(
)
z
,
y
,
x
(
F
M
P
=

## Slide 35: A Simplification Example
Simplify F
Writing the minterm expression:
F = A’ B’ C + A B’ C’ + A B C’ + AB’C + ABC
Simplifying using Boolean algebra:
F =
Notes: F = A’ B’ C + A (B’ C’ + B C’ + B’ C + B C)
= A’ B’ C + A[B’(C’+C) +B(C’+C)]
= A’ B’ C + A[B’.1+B.1]
= A’ B’ C + A.1
= A’ B’ C + A
= B’C + A

## Slide 36: 2-4 Circuit Optimization
Goal: To obtain the simplest implementation for a given function
Optimization requires a cost criterion to measure the simplicity of a circuit
Distinct cost criteria we will use:
  Literal cost (L)
  Gate input cost (G)
  Gate input cost with NOTs (GN)
Notes: Other possible criteria: Speed
Power consumption
Size and cost

## Slide 37: Literal Cost
Literal – a variable or its complement
Literal cost – the number of literal appearances in a Boolean expression corresponding to the logic circuit diagram
Examples (all the same function):
  F = BD + AB’C + AC’D’ L = 8
  F = BD + AB’C + AB’D’ + ABC’ L =
  F = (A + B)(A + D)(B + C + D’)( B’ + C’ + D) L =
  Which solution is best?
Notes: 2nd Literal Cost = 11
3rd Literal Cost = 10
The first solution is best NOTE: all these represent the same function: f=Sum m(5,7,8,10,11,12,13,15)

## Slide 38: Gate Input Cost
Gate input costs - the number of inputs to the gates in the implementation corresponding exactly to the given equation or equations. (G - inverters not counted, GN - inverters counted)
For SOP and POS equations, it can be found from the equation(s) by finding the sum of:
  all literal appearances
  the number of terms excluding single literal terms,(G) and
  optionally, the number of distinct complemented single literals (GN).
Example:
  F = BD + A C + A G = 8, GN = 11
  F = BD + A C + A + AB G = , GN =
  F = (A + )(A + D)(B + C + )( + + D) G = , GN =
  Which solution is best?
D
B
C
B
B
D
C
B
D
B
C
Notes: G = 15, GN = 18 (second value includes inverter inputs)
G = 14, GN = 17
1st solution is best

## Slide 39: Cost Criteria (continued)
Example:
F = A B C + A’B’C’
L = 6 G = 8 GN = 11
F = (A +C’)(B’+ C)(A’+B)
L = 6 G = 9 GN = 12
Same function and same literal cost
But first circuit has better gate input count and better gate input count with NOTs
Select it!
A
B
C
F
F
A
B
C
Notes: Proof: ABC+A’B’C’ =(A+C’)(B’+C)(A’+B)
Start with right expression:
(A+C’)(B’+C)(A’+B)
=(AB’+AC+B’C’)(A’+B)
=(AC+B’C’)(A’+B) (consensus)
=A’B’C’+ABC

## Slide 40: Karnaugh Maps (K-maps)
Maurice Karnaugh (October 4, 1924) is an American physicist, who introduced the Karnaugh map while working at Bell Labs
Source: http://en.wikipedia.org/wiki/File:Eugeneguth.jpg

## Slide 41: Karnaugh Maps (K-map)
A K-map is a collection of squares
  Each square represents a minterm
  The collection of squares is a graphical representation of a Boolean function
  Adjacent squares differ in the value of one variable
  Alternative algebraic expressions for the same function are derived by recognizing patterns of squares
The K-map can be viewed as
  A reorganized version of the truth table
  A topologically-warped Venn diagram as used to visualize sets in algebra of sets

## Slide 42: Two Variable Maps
Truth Table of F(x,y)
x y F
0 0 0 m0
0 1 1 m1
0 0 m2
1 1 1 m3
y = 0
y = 1
x = 0
x = 1
m
1 =
y
x
m
3 =
y
x
K-map
y = 0
y = 1
x = 0
x = 1
0
1
1
0
F= m1 +m3 = x’y + xy = (x+x’)y = y
m
0 =
y
x
m
2 =
y
x

## Slide 43: K-Map Function Representation
Example: G(x,y) = xy’ + x’y + xy
Simplify using theorems:
  G = x (y’+y) + x’y = x.1 +x’y = x + x’y = x + y
Simplify using K-map: cover adjacent cells
G
y = 0
y = 1
x = 0
0
1
x = 1
1
1

## Slide 44: Three Variable Maps
A three-variable K-map:
Where each minterm corresponds to the product terms:
Note that if the binary value for an index differs in one bit position, the minterms are adjacent on the K-Map
m0
m1
m3
m2
m4
m5
m7
m6
yz=00
yz=01
yz=11
yz=10
x=0
x=1
yz=00
yz=01
yz=11
yz=10
x=0
x=1
z
y
x
z
y
x
z
y
x
z
y
x
z
y
x
z
y
x
z
y
x
z
y
x

## Slide 45: Three variable K-map
y
y z
z
1
0
2
4
3
5
6
7
x
x

## Slide 46: Example Functions
By convention, we represent the minterms of F by a "1" in the map and a “0” otherwise
Example:
Example:
x
y
1
0
2
4
3
5
6
7
z
1
0
2
4
3
5
6
7
z
y
x
1
1
1
1
F
G
Notes: F=XY’+X’Y
G=XZ’+YZ
x
y
1
0
2
4
3
5
6
7
1
1
1
1
z

## Slide 47: Example: Combining Squares
Example: Let
Applying the Minimization Theorem three times:
Thus the four terms that form a 2 × 2 square correspond to the term "y".
x
y
1
0
2
4
3
5
6
7
1
1
1
1
z
y
=
z
y
yz
+
=
z
y
x
z
y
x
z
y
x
z
y
x
)
z
,
y
,
x
(
F
+
+
+
=
m2 +m3 +m6 +m7

## Slide 48: Three Variable Maps
z)
y,
F(x,
= ?
Use the K-Map to simplify the following Boolean function
x
y
1
0
2
4
3
5
6
7
z
Notes: F = z + x’y
y
1
1
x
z
1
1
1
F = Z + X’Y

## Slide 49: Four-Variable Maps
Variables A,B,C and D
C
A
D
B
8
9
10
11
12
13
14
15
0
1
3
2
5
6
4
7
Notice: only one variable changes for adjacent boxes

## Slide 50: Four-Variable Maps
Example F= =m (0,2,3,5,6,7,8,10,13,15)
8
9
10
11
12
13
14
15
0
1
3
2
5
6
4
7
B
C
D
A
1
1
1
1
1
1
1
1
1
1
F= BD + A’C + B’D’

## Slide 51: Four-Variable Map Simplification
)
8,10,13,15
2,4,5,6,7,
(0,
Z)
Y,
X,
F(W,
m
S
=
F=
A
D
B
8
9
10
11
12
13
14
15
0
1
3
2
5
6
4
7
Notes: F = XZ + X'Z‘ + w’x
’
1
1
1
1
X
Y
Z
W
1
1
1
1
1
1
F= XZ + W’X + X’Z’
1
1
1
1
X
Y
Z
W
1
1
1
1
1
1
F= XZ + W’Z’ + X’Z’

## Slide 52: 2-5 Map Manipulation: Systematic Simplification
A Prime Implicant is a product term obtained by combining the maximum possible number of adjacent squares in the map into a rectangle with the number of squares a power of 2.
A prime implicant is called an Essential Prime Implicant if it is the only prime implicant that covers (includes) one or more minterms.
Prime Implicants and Essential Prime Implicants can be determined by inspection of a K-Map.

## Slide 53: Example of Prime Implicants
D
B
C
B
1
1
1
1
1
1
B
D
A
1
1
1
1
1
Find ALL Prime Implicants
ESSENTIAL Prime Implicants
C
BD
CD
BD
Minterms covered by single prime implicant
D
B
1
1
1
1
1
1
B
C
D
A
1
1
1
1
1
AD
B
A

## Slide 54: Optimization Algorithm
Find all prime implicants.
Include all essential prime implicants in the solution
Select a minimum cost set of non-essential prime implicants to cover all minterms not yet covered

## Slide 55: Previous example: Minimum SOP
Pick all Essential Prime Implicants: B’D’, BD
Add non essential prime implicants: CD (o B’C), AD (or AB’)
CD
D
B
1
1
1
1
1
1
B
C
D
A
1
1
1
1
1
AD
F= B’D’+BD +CD+AD

## Slide 56: Selection Rule Example
Simplify F(A, B, C, D) given on the K-map.
1
1
1
1
1
1
1
B
D
A
C
1
1
1
1
1
1
1
1
1
B
D
A
C
1
1
Essential
Minterms covered by essential prime implicants
Selected
Minterm covered by one prime implicant
F = ?
Notes: F= A’B+A’CD+AC’D+B’C’D’

## Slide 57: Exercise
Find all prime, essential implicants for:
  Give the minimized SOP implementation
B
D
A
C
Notes: Prime Implicants are AB, B C' D', A' C' D', A' B' D', A' B' C, A' C D, B C D.

## Slide 58: Don't Cares in K-Maps
Sometimes a function table or map contains entries for which it is known:
  the input values for the minterm will never occur, or
  The output value for the minterm is not used
In these cases, the output value need not be defined
Instead, the output value is defined as a “don't care”
By placing “don't cares” ( an “x” entry) in the function table or map, the cost of the logic circuit may be lowered.
Example 1: A logic function having the binary codes for the BCD digits as its inputs. Only the codes for 0 through 9 are used. The six codes, 1010 through 1111 never occur, so the output values for these codes are “x” to represent “don’t cares.”

## Slide 59: Don’t care example
BCD code on a seven segment display:
WXYZ | Digit | a | b
0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 1010 1011 1100 1101 1110 1111 | 0 1 2 3 4 5 6 7 8 9 - | 1 0 1 1 0 1 1 1 1 1 X X X X X X | 1 1 1
a=Σm(0,2,3,5,6,7,8,9)+ Σ d(10,11,12,13,14,15)
X
Y
Z
W
1
1
1
1
1
1
1
X
X
X
X
X
X
1
a=?
a b c d… g
W X Y Z
?
Input (BCD)
outputs
Notes: F=W+Y+XZ+X’Z’
X
Y
Z
W
1
1
1
1
1
1
1
X
X
X
X
X
X
1

## Slide 60: Find SOP for segment “a”
a=Σm(0,2,3,5,6,7,8,9)+ Σ d(10,11,12,13,14,15)
X
Y
Z
W
1
1
1
1
1
1
1
X
X
X
X
X
X
1
a=?
Notes: F=W+Y+XZ+X’Z’
X
Y
Z
W
1
1
1
1
1
1
1
X
X
X
X
X
X
1

## Slide 61: Product of Sums Example
Find the optimum POS solution:
  Hint: Use F’ and complement it to get the result.
Notes: F' = B' D' + A' B
F = (B + D)(A + B')

## Slide 62: Product of Sums Example
Find the optimum POS solution:
1
1
1
1
1
1
1
x
x
x
0
0
0
0
0
0
F’=A’B + B’D’+A’C’
Thus F=(A+B’) (B+D) (A+C)
Find prime implicants for F’
Use DeMorgan’s to find F as POS
B
C
D
A
A’B, B’D’, A’C’;
Notes: F' = B' D' + A' B
F = (B + D)(A + B')

## Slide 63: Exercises with don’t cares
F(A,B,C,D)=Σm(2,5,8,10,13,14) +Σd(0,1,6)
Write F as minimized SOP:
  F=
Write F as minimized POS
  F=
Notes: F= CD’+B’D’+BC’D
And F’=CD+B’D+BC’D’, thus (e.g. DeMorgan):
F=(C’+D’)(B+D’)(B’+C+D)
B
C
D
A
1
1
1
1
1
1
X
X
X
B
C
D
A
1
1
1
1
1
1
X
X
X

## Slide 64: Exercise: Design a 2-bit comparator
Design a circuit that has two 2–bit numbers N1 and N2 as inputs, and generates three outputs to indicate if N1<N2, N1=N2 and N1>N2.
Design the circuit as minimized SOP
N1
N2
F1
F2
F3
(N1<N2)
(N1>N2)
A
B
C
D
N1=AB
N2=CD
(N1=N2)
Notes: See Katz, Ex. 2.3.4 (P75; 1st ed)

## Slide 65: Design a 2-bit comparator - Solution

## Slide 66: Design a 2-bit comparator - Solution

## Slide 67: 2-8 Other Gate Types
Why?
  Easier to implement on a chip than the AND, OR gates
  Convenient conceptual representation
(Intel)
A
B
A
B

## Slide 68: Other Gate Types: overview
A B BUF NAND NOR XOR XNOR
0 0 0 1 1 0 1
0 1 0 1 0 1 0
1 0 1 1 0 1 0
1 1 1 0 0 0 1
A
A
B
A
B
A
B
A
B

## Slide 69: Buffer
A buffer is a gate with the function F = X:
In terms of Boolean function, a buffer is the same as a connection!
So why use it?
  A buffer is an electronic amplifier used to improve circuit voltage levels and increase the speed of circuit operation.
X
F

## Slide 70: NAND Gates
The NAND gate is the natural implementation for CMOS technology in terms of chip area and speed.
Universal gate - a gate type that can implement any Boolean function.
The NAND gate is a universal gate:
  NOT implemented with NAND:
  AND implemented with NAND gate:
  OR using NAND:
X
Y
Z
Notes: NOT: A=B and OUT=(AB)’
NAND: AND + NOT
NOR: DeMorgan’s: (A+B) = (A+B)’’= (A’B’)’

## Slide 71: NOR Gates
Similary as the NAND gate, the NOR gate is a Universal gate
Universal gate - a gate type that can implement any Boolean function.
With a NOR gate one can implement
  A NOT
  An AND
  An OR
A
B
Notes: NOT: A=B and OUT=(A+B)’
OR: NOR+ NOT
NAND : DeMorgan’s: (AB) = (AB)’’= (A’+B’)’

## Slide 72: 2-9 Exclusive OR/ Exclusive NOR
The eXclusive OR (XOR) function is an important Boolean function used extensively in logic circuits:
  Adders/subtractors/multipliers
  Counters/incrementers/decrementers
  Parity generators/checkers
The eXclusive NOR function (XNOR) is the complement of the XOR function
XOR and XNOR gates are complex gates (built from simpler gates, such as AND, Not, etc).

## Slide 73: Truth Tables for XOR/XNOR
XOR
The XOR function means:
X OR Y, but NOT BOTH
The XNOR function also known as the equivalence function, denoted by the operator 
X
Y
X
Å
Y
0
0
0
0
1
1
1
0
1
1
1
0
X
Y
0
0
1
0
1
0
1
0
0
1
1
1
or X
º
Y
(X
Å
Y)
XNOR
Notes: Because it is defined as X Y + X’ Y’ that equals 1 if and only if X = Y implying X is equivalent to Y.

## Slide 74: XOR Implementations
The simple SOP implementation uses the following structure:
A NAND only implementation is:
X
Y
X
Y
X
Y
X
Y
Y
X
Y
X
Y
X
+
=
Å
Notes: Prove: XY’+X’Y = (XX’+XY’+YY’+X’Y)= X(X’+Y’) +Y(X’+Y’) =X.(XY)’+Y(XY)’
=[(X.(XY)’)’.(Y(XY)’)’]’’
Nand: Verify
(((XY)’.X)’. ((XY)’.Y)’)’
= ((XY)’.X)+((XY)’.X)
=(X’+Y’)X + (X’+Y’)Y
=XY’+X’Y

## Slide 75: Odd and Even Functions
The odd and even functions on a K-map form “checkerboard” patterns.
The 1s of an odd function correspond to minterms having an index with an odd number of 1s.
The 1s of an even function correspond to minterms having an index with an even number of 1s.
Implementation of odd and even functions for greater than four variables as a two-level circuit is difficult, so we use “trees” made up of :
  2-input XOR or XNORs
  3- or 4-input odd or even functions

## Slide 76: Example: Odd Function Implementation
Design a 3-input odd function F = X Y Z with 2-input XOR gates
Factoring, F = (X Y) Z
The circuit:
+
+
+
+
X
Y
Z
F

## Slide 77: Example: 4-Input Function Implementation
Design a 4-input odd function F = W X Y Z with 2-input XOR and XNOR gates
Factoring, F = (W X) (Y Z)
The circuit:
+
+
+
+
+
+
W
X
Y
F
Z

## Slide 78: Parity Generators and Checkers
In Chapter 1, a parity bit added to n-bit code to produce an n + 1 bit code:
  Add odd parity bit to generate code words with even parity
  Add even parity bit to generate code words with odd parity
  Use odd parity circuit to check code words with even parity
  Use even parity circuit to check code words with odd parity

## Slide 79: Parity Generators and Checkers
Example: n = 3. Generate even parity code words of length four with odd parity generator:
Check even parity code words of length four with odd parity checker
Operation: (X,Y,Z) = (0,0,1) gives (X,Y,Z,P) = (0,0,1,1) and E = 0. If Y changes from 0 to 1 between generator and checker, then E = 1 indicates an error.
X
Y
Z
P
0
0
1
=1
0
0
1
1
0
X
Y
Z
E
P
Error
1
1

## Slide 80: 2-10 Hi-Impedance Outputs
Logic gates introduced thus far
  have 1 and 0 output values,
  cannot have their outputs connected together, and
  transmit signals on connections in only one direction.
Three-state (or Tri-state) logic adds a third logic value, Hi-Impedance (Hi-Z), giving three states: 0, 1, and Hi-Z on the outputs.
What is a Hi-Z value?
  The Hi-Z value behaves as an open circuit
  This means that, looking back into the circuit, the output appears to be disconnected.

## Slide 81: The Tri-State Buffer
For the symbol and truth table, IN is the data input, and EN, the control input.
For EN = 0, regardless of the value on IN (denoted by X), the output value is Hi-Z.
For EN = 1, the output value follows the input value.
Variations:
  Data input, IN, can be inverted
  Control input, EN, can be inverted
  by addition of “bubbles” to signals.
IN
EN
OUT
EN
IN
OUT
0
X
Hi-Z
1
0
0
1
1
1
Symbol
Truth Table
OUT= IN.EN

## Slide 82: Tri-State Logic Circuit
Data Selection Function: If s = 0, OL = IN0, else OL = IN1
Performing data selection with 3-state buffers:
Since EN0 = S and EN1 = S, one of the two buffer outputs is always Hi-Z plus the last row of the table never occurs.
IN0
IN1
EN0
EN1
S
OL
OL= IN0.S’ + IN1.S

## Slide 83: Exercise
Implement a gate with two three-state buffers and two inverters:
  F = X Y=XY’+X’Y
Å
X
X’
EN0=Y’
EN1=Y
Y
F

## Slide 84: Other usage of Tristate buffers
Tristate bus connecting multiple chips:
Processor
EN1
To bus
from bus
Memory
EN2
To bus
from bus
Video
EN3
To bus
from bus
Shared bus