## Slide 1: Chapter 5 ----Sequential Circuits

## Slide 2: Combinational and Sequential Circuits
Up to now we have discussed combinational circuits.
In many cases, one can reduce the complexity of the hardware by using sequential circuits.
Sequential circuits allow for more flexible and more sophisticated circuit realizations with richer behavior and dynamics.

## Slide 3: 5-1 Sequential circuit block diagram
Combina-tional
Logic
Inputs
Outputs
Storage Elements
State
(or present state)
Next
State
CLOCK
Synchronous machine
Combinatorial Logic gives:
  Next state function Next State = f(Inputs, State)
  Output function

## Slide 4: Types of Sequential Circuits
Synchronous
  Behavior defined from knowledge of its signals at discrete instances of time
  Storage elements observe inputs and can change state only in relation to a timing signal (clock pulses from a clock)
Asynchronous
  Behavior defined from knowledge of inputs an any instant of time and the order in continuous time in which inputs change
The synchronous abstraction makes complex designs tractable!
t1 t2 t3 t4
t1 t2 t3 t4

## Slide 5: Moore and Mealy Models
Sequential Circuits or Sequential Machines are also called Finite State Machines (FSMs). Two formal models exist:
Moore Model
  Named after E.F. Moore
  Outputs are only a function of states
Mealy Model
  Named after G. Mealy
  Outputs are a function of inputs and states

## Slide 6: Types of Sequential Circuits Illustra
Moore machine:
  Outputs = h(State)
Mealy machine
  Outputs = g(Inputs, State)
Combina-tional
Logic
Storage Elements
Inputs
State
(or present state)
Next
State
Outputs
Comb.
logic
CLOCK
Mealy

## Slide 7: 5-2 Storing information: Latches
How to store information?
Signal B=A appears after a short delay:
tpd
A
B
tpd
C
Reinforces the input A
tpd = propagation delay
A
C= A
B=A
tpd
tpd
Use feedback:

## Slide 8: Latches: Cross-coupled NORs
1
2
A=0
B=A=1
C= A=0
0
0
How to change contents A from 0 to 1: apply “1” to the first input
Set
Hold or memory
A=0 is memorized
We have written “1” into the latch: “set” operation
0
1
0
0
0
1
2
1
0
1
1
0
Making the input go to “0” again will memorize the output C=“1”
1
1
1
0
0

## Slide 9: Basic (NOR) S – R Latch
Function Table:
This element is also the basic building block in SRAM memories
S (set)
R (reset)
Q
Q
S R Q Q
0 0
0 1
0
1 1
hold, no change
0 1 Reset
1 0 Set
0 0 not allowed, unstable (Q=Q)

## Slide 10: Basic (NOR) S – R Latch
Function Table:
This element is also the basic building block in SRAM memories
S (set)
R (reset)
Q
Q
S R Q Q
0 0
0 1
0
1 1
hold, no change
0 1 Reset
1 0 Set
0 0 not allowed, unstable (Q=Q)

## Slide 11: Exercise: Basic (NOR) S – R Latch
Time sequence behavior:
R
S
Q
Q
Comment
0
0
?
?
Stored state unknown
0
1
1
0
“Set” Q to 1
0
0
1
0
Now Q “remembers” 1
1
0
0
1
“Reset” Q to 0
0
0
0
1
Now Q “remembers” 0
1
1
0
0
Both go low
0
0
?
?
Unstable!
Time
1
2
S
R
Q
Q

## Slide 12: Timing waveforms of NOR S-R latch
1
2
S
R
Q
Q
S
R
0
0
not allowed
Q
Q
1
0
tpd
set
reset
unstable
No change

## Slide 13: Clocked (NOR) S-R Latch
1
2
Q
Q
S
R
Clk
Clk=0: input has no effect: latch is always in “hold” mode
Clk=1: latch is a regular S-R latch

## Slide 14: Clocked S - R Latch (continued)
The Clocked S-R Latch can be described by a table:
The table describes what happens after the clock [at time (t+1)] based on:
  current inputs (S,R) and
  current state Q(t).
1
2
S
R
Q
Q
Clock
0 x x
0 0
1 0 1
1 1 0
1 1 1
Q(t) no change
Q(t) no change
Q(t+1) = 0, Reset
Q(t+1) = 1, Set
Undefined
C S R Next state Q(t+1)

## Slide 15: Function table of the (NAND) S - R latch
S R Q Q
1 1
0 1
0
0 0
S = 0, R = 0 is forbidden as input pattern
Function table:
hold, no change
1 0 Set
0 1 Reset
1 1 not allowed, unstable (Q=Q=1)
Q
S (set)
R (reset)
Q

## Slide 16: Latch with NAND
Q
1
1
Q
When both S=R=1: the NAND gates act as inverters and the circuit implements two inverters: “hold mode”
Q
Q
A
=
A
1
A
A
S
R
C
Q
Q
S
R
Clocked latch:
0 x x
0 0
1 0 1
1 1 0
1 1 1
Q(t) no change
Q(t) no change
Q(t+1) = 0, Reset
Q(t+1) = 1, Set
Q=Q’=1 Undefined
C S R Next state Q(t+1)

## Slide 17: D Latch (Delay latch)
S-R Latch can be used for at D Latch:
C
D
Q
Q
D Q(t+1)
0 0
1 1
Function table D latch:
S R Q+ Q+
0 0 hold,
0 1 0 1
0 1 0
1 1 0 0
SR latch:
D
Q
C
Q
Q(t+1)

## Slide 18: Latch issues
Latches can cause serious timing problems (races) in sequential circuits
  Due to the fact that a latch is “transparent” when the clock C = 1
The timing problems can be prevented by using “Flip-Flops”

## Slide 19: The Latch Timing Problem (continued)
Similar timing problems in the sequential circuits:
Combina-tional
Logic
D Latch
(storage)
Inputs
Outputs
State
Next State
X0
The state should change only once every new clock cycle:
  C=1:
    Now the current state becomes X1 and a new state is generated by the combinational logic circuit: X2.
    However, if C=1, the new “next state” X2 will create a new current state X2!, etc…
X1
X0
X2
X2
C=0
X1
X1
X1
X2
X2
X3
1

## Slide 20: How to solve the timing problem: use Flip-Flops
A solution to the latch timing problem is to break the closed path from In to Out within the storage element
C
D
Q
Q
In
Out
C: 0 1
C
D
Q
Q
In
Out
C: 0 1
D-Latch
D-Flip-Flop
In
C
Out
In
C
Out

## Slide 21: S-R Master-Slave Flip-Flop - review
Consists of two clocked S-R latches in series with the clock on the second latch inverted
C
S
R
Q
Q
Q
Q
C
Master Latch
Slave Latch
Master Latch responds to input (Y changes)
Slave latch is inactive: Q unchanged
Master Latch is inactive
Slave latch responds to inputs Y, Y’;
Output Q changes
C
R
Q
Q
C
S
R
S
Y
Y’

## Slide 22: Symbol: Master-Slave Flip-Flop
C
S
R
Q
Q
Q
Q
C
R
Q
Q
C
S
R
S
Y
Y’
C
Notice; the output changes when the clock C goes low.
Symbol:
S
C
R
Q
Q
Sometimes one adds:
To indicate that the input responds when C=1, but the output changes when C goes to 0

## Slide 23: Timing diagram of a (Nor) S-R Master-Slave Flip-Flop
C
S
R
Y
Q
Slave out
Master out
Master
active
Slave
active
Output changes at neg. clock edge:
Negative edge-trigger FF
0
0
C
S
R
Q
Q
Q
Q
C
R
Q
Q
C
S
R
S
Y
Y’
S
C
R
Q
Q

## Slide 24: Flip-Flop Problem: 1’ catching
C
S
R
Y
Q
Slave out
Master out
Master
active
Slave
active
1’ catching
wrong output
should have been 0
C
S
R
Q
Q
Q
Q
C
R
Q
Q
C
S
R
S
Y
Y’
Glitch

## Slide 25: Flip-Flop Solution: Edge-triggered
An edge-triggered flip-flop changes values at the clock edge (transition):
  responds to its input at a well-defined moment (at the clock-transition)
  ignores the pulse while it is at a constant level
Positive edge-triggered
Negative edge-triggered
Clock
In
The value of the input at the clock transition (negative or positive) determines the output
ignored

## Slide 26: Flip-Flop Solution
A master-slave D flip-flop which exhibits edge-triggered behavior can be used:
  Replacing the first clocked S-R latch with a clocked D latch or
  Adding a D input and inverter to a master-slave S-R flip-flop
C
S
R
Q
Q
C
R
Q
Q
C
S
R
Q
S
Q
C
S
R
Q
Q
C
Q
Q
C
D
Q
D
Q

## Slide 27: Edge-Triggered D Flip-Flop
The 1s-catching behavior is not present with D replacing S and R inputs
The change of the D flip-flop output is associated with the negative edge at the end of the pulse:
It is called a negative-edge triggered flip-flop
C
S
R
Q
Q
C
Q
Q
C
D
Q
D
Q

## Slide 28: No 1’s catching in the edge-triggered D Flip-Flops
C
S
R
Q
Q
C
Q
Q
C
D
Q
D
Q
C
D
Y
Q
Slave out
Master out
Master
active
Slave
active
no 1’ catching
correct output
Y

## Slide 30: Standard Symbols for Storage Elements
Latches:
Master-Slave: Postponed output indicators
Edge-Triggered: Dynamic indicator
D with 0 Control
Triggered D
(a) Latches
S
R
SR
SR
S
R
D
C
D with 1 Control
D
C
(b) Master-Slave Flip-Flops
D
C
Triggered D
Triggered SR
S
R
C
D
C
Triggered SR
S
R
C
(c) Edge-Triggered Flip-Flops
Triggered D
D
C
Triggered D
D
C
Input samples when C=1 but output changes when C goes 0
Input samples when C=0 but output changes when C goes 1

## Slide 31: Exercise

## Slide 32: Timing diagram of a (Nor) S-R Master-Slave Flip-Flop
C
Slave out
Master
active
Y
Master out
Q
S
C
R
Q
Q
S
R
Slave
active
Master
active
Y’
C
S
R
Q
Q
Q
Q
C
R
Q
Q
S
Y
Y’
S
R
C
=
undefined
undefined
undefined

## Slide 33: Direct Inputs
At power up or at reset, all or part of a sequential circuit usually is initialized to a known state before it begins operation
This initialization is often done outside of the clocked behavior of the circuit, i.e., asynchronously.
Direct R and/or S inputs that control the state of the latches within the flip-flops are used for this initialization.
For the example flip-flop shown
  0 applied to R resets the flip-flop to the 0 state
  0 applied to S sets the flip-flop to the 1 state
D
C
S
R
Q
Q

## Slide 34: Direct inputs: active-low or active-high
D flip-flop with active-low direct inputs :
Active high direct inputs:
D
C
S
R
Q
Q
D
C
S
R
Q
Q
S R C D Q Q’
0 1 x x 1 0
0 x x 0 1
1 1 0 0 1
1 1 1 1 0
S R C D Q Q’
0 1 x x 0 1
0 x x 1 0
0 0 0 0 1
0 0 1 1 0
Direct inputs

## Slide 35: Timing Constraints (Section 6.3)
0101101101100110

## Slide 36: Flip-Flop Timing: Setup and Hold times – critical time constraints!
Proper operation requires strict timing rules:
  Minimum clock pulse width: tw (tWH, tWL)
  Set-up time tS: minimum amount of time that the input signal must be present prior to occurrence of the clock transition that causes the output to change
  Hold time th: time the input must be kept after the clock transition

## Slide 37: Case of Edge triggered Flip-Flop: set-up and hold times
Negative edge-triggered
C
tS
th
In (D)
Out
Propagation delay
(measured from clock transition):
tp,min
tp,max
C
D
Q
Q
In
Out
C

## Slide 38: Flip-Flop Timing: Setup and Hold times
tS
th
Master-Slave S/R flip-flop (output changes at falling clock):
C
S/R

## Slide 39: Metastability
When one violates the set-up or hold times, the flip-flop can enter a metastable state!
Flip-flops can have three states:
  State 0 (Stable)
  State 1 (Stable)
  Metastable state
Compare to a ball on a hill:
After a short, non deterministic time the ball will roll to either state 0 or 1!
This will give unpredictable behavior

## Slide 40: Metastable behavior
Example of metastable behavior:
After a while the flip-flop will go into a stable state (randomly).
If this happens before the next clock edge, the actual circuits will see a defined input.
The longer the clock period is the less chance of synchronization failure.
Or use two synchronization flip-flops in series
Eventually, the flip-flop will settle
(Oscilloscope trace)
Logic 1 (Hi)
Logic 0 (Lo)
metastable

## Slide 41: Exercise solution
Complete the waveforms below
1st stage active
2nd stage active

## Slide 42: Exercise (continued)
Modify this circuit to give a DIRECT (i.e. asynchronous) active-high reset input (make minimal changes to the circuit: add the required reset input)

## Slide 43: Exercise - solution
The following timing diagram gives the input and clock for a SR device. Draw the output waveforms assuming the device is (a) clocked D-latch, (b) a Negative edge triggered Master Slave D flip-flop, and (c) a Positive edge triggered D flip-flop.
D- Neg.
Edge

## Slide 44: Exercise - solution
The following timing diagram gives the input and clock for a SR device. Draw the output waveforms assuming the device is (a) clocked D-latch, (b) a Negative edge triggered Master Slave D flip-flop, and (c) a Positive edge triggered D flip-flop.
D- Neg.
Edge

## Slide 45: 5-4 Sequential Circuit Analysis
Consider the following circuit:
C
D
Q
Q’
C
D
Q
Q'
y
x
A
A
B
CLK
What does it do?
How do the outputs change when an input arrives?
input
states
output
Notes: Mealy machine: x goes into the output circuit

## Slide 46: Sequential Circuit Model
General Model
  Current or Present State at time (t) is stored in an array of flip-flops.
  Next State is a Boolean function of State and Inputs.
  Outputs at time (t) are a Boolean function of State (t) and (sometimes) Inputs (t).
Combina-tional
Logic
Storage (D Flip-flops)
Inputs
State
(or current state)
Next
State
Outputs
Comb.
logic
CLOCK
Mealy

## Slide 47: Previous Example (from Fig. 5-15)
Input: x(t)
Output: y(t)
State: (A(t), B(t))
  Example: (AB)= (01), (10)
Next State:
  (DA(t), DB(t))
  = (A(t+1), B(t+1))
C
D
Q
Q’
C
D
Q
Q'
y
x
A
A
B
CLK
Output logic
Next State
DA
DB
Is this a Moore or Mealy machine?
Comb. Input logic
Present state
Notes: Mealy machine: x goes into the output circuit

## Slide 48: Steps for Analyzing a Sequential Circuit
Find the input equations (DA, DB) to the flip-flops (next state equations) and the output equation.
Derive the State Table (describes the behavior of a sequential circuit).
Draw the State Diagram (graphical description of the behavior of the sequential circuit).
Simulation

## Slide 49: Step 1: Input and output equations
Boolean equations for the inputs to the flip flops:
  DA = A(t)x(t)+B(t)x(t)
  DB = A(t)x(t)
Output y
  y(t) = x(t)(B(t) + A(t))
C
D
Q
Q’
C
D
Q
Q'
y
x
A
A
B
CLK
Next State
Output
DA
DB
Present state

## Slide 50: Step 2: State Table Characteristics
The state table: shows what the next state and the output will be as a function of the present state and the input:
The State Table can be considered a truth table defining the combinational circuits:
  the inputs are Present State, Input,
  and the outputs are Next State and Output
Present State
Input
Next State
Output
Inputs of the combinational circuit
Outputs of the table

## Slide 51: State Table
For the example: A(t+1) = A(t)x(t) + B(t)x(t)
        B(t+1) =A (t)x(t)
        y(t) =x (t)(B(t) + A(t))
Present State
Input
Next State
Output
A(t) B(t)
x(t)
A(t+1) B(t+1)
y(t)
0 0
0
0 0
1
0 1
0
0 1
1
1 0
0
1 0
1
1 1
0
1
1
1
23 rows
(2m+n) rows
m: no. of FF
n: no. of inputs
Inputs of the table
Outputs of the table
0 0
0
0 1
0
0 0
1
1 1
0
0 0
1
1 0
0
0 0
1
1 0
0

## Slide 52: Alternate State Table
The previous (1-dimensional table) can become quite lengthy with 2m+n rows (m=no. of FF; n=no. of inputs)
Alternatively, a 2-dimensional table has the present state in the left column and inputs across the top row
  A(t+1) = A(t)x(t) + B(t)x(t)
  B(t+1) =A (t)x(t)
  y(t) =x (t)(B(t) + A(t))
0 0 0 1
0 0 1 1
0 0
1 0
0 0 1 0
0 0
1 0
1 0
1 0
Present
State
Next State
x(t)=0 x(t)=1
Output
x(t)=0 x(t)=1
A(t) B(t)
A(t+1)B(t+1) A(t+1)B(t+1)
y(t) y(t)
0 0
0 1
1 0
1 1
2m

## Slide 53: Example 1(from Fig. 5-15) (continued)
Where in time are inputs, outputs and states defined?
0
0
0
0
1
1
1
0

## Slide 54: Step 3: State Diagrams
The sequential circuit function can be represented in graphical form as a state diagram with the following components:
  A circle with the state name in it for each state
  A directed arc from the Present State to the Next State for each state transition
  A label on each directed arc with the Input values which causes the state transition, and
  A label:
    In each circle with the output value produced, or
    On each directed arc with the output value produced.
State
State
In/out
State
out
in
in

## Slide 55: State diagram convention
Moore Machine:
State
out
in
Moore type output depends only on state
to next state
01
1
1
Mealy Machine:
    Mealy type output depends on state and input
State
In/out
01
x=1/y=0
AB
y
x
Example:
01
x/y’

## Slide 56: State Diagram for the example
Graphical representation of the state table:
A B
0 0
0 1
1 1
1 0
x=0/y=1
x=1/y=0
x=1/y=0
x=0/y=1
x=0/y=1
x=1/y=0
Present State
Input
Next State
Output
A(t) B(t)
x(t)
A(t+1) B(t+1)
y(t)
0 0
0
0 0
0
0 0
1
0 1
0
0 1
0
0 0
1
0 1
1
1 1
0
1 0
0
0 0
1
1 0
1
1 0
0
1 1
0
0 0
1
1
1
1
1 0
0
x=0/y=0
x=1/y=0
Notes: Type: Mealy

## Slide 57: State Diagram of a SR Flip-flop
S R Q+
0 0
0 1
0
1 1
Q
0
1
-
Function table
S
C
R
Q
Q
State Diagram:
0
1
10
01
00
10
01
00
SR
0
1
10
01
0X
X0
Or

## Slide 58: Equivalent State Definitions
Two states are equivalent if their response for each possible input sequence is an identical output sequence.
Alternatively, two states are equivalent if their outputs produced for each input symbol is identical and their next states for each input symbol are the same or equivalent.

## Slide 59: Equivalent State Example
Consider the following state diagram:
Which states are equivalent?
S2
S3
1/0
0/1
1/0
0/0
S0
S1
1/0
0/1
1/0
0/1
Notes: S2 and S3

## Slide 60: Equivalent State Example
Equivalent states in the state diagram:
For states S2 and S3,
  the output for input 0 is 1 and the for input 1,
  the output is 0
  the next state for input 0 is S0 and for input 1 is S2.
  By the alternative definition, states S2 and S3 are equivalent.
S2
S3
1/0
0/1
1/0
0/0
S0
S1
1/0
0/1
1/0
0/1

## Slide 61: Equivalent State Example
Replacing S2 and S3 by a single state gives state diagram:
S2
1/0
0/0
S0
S1
1/0
0/1
1/0
0/1
S2
S3
1/0
0/1
1/0
0
S0/0
S1
1/0
0/1
1
0/1

## Slide 62: Equivalent State Example
Are there other equivalent states?
Examining the new diagram, states S1 and S2 are equivalent since
  their outputs for input 0 is 1 and input 1 is 0, and
  their next state for input 0 is both S0 and for input 1 is both S2,
Replacing S1 and S2 by a single state gives state diagram:
S2
1/0
0/0
S0
S1
1/0
0/1
1/0
0/1
0/0
S0
S1
1/0
0/1
1/0

## Slide 63: Exercise: Derive the state diagram of the following Circuit
Logic Diagram:
Clock
Reset
D
Q
C
Q
R
D
Q
C
Q
R
D
Q
C
Q
R
A
B
C
Z
Moore or Mealy?
What is the reset state?
•
•
5V
Notes: Moore Machine
Reset state: 000

## Slide 64: Exercise: Derive the state diagram of the following Circuit
Logic Diagram:
Clock
Reset
D
Q
C
Q
R
D
Q
C
Q
R
D
Q
C
Q
R
A
B
C
Z
Moore or Mealy?
What is the reset state?
•
•
5V
Notes: Moore Machine
Reset state: 000

## Slide 65: Step1: Flip-Flop Input Equations
Variables
  Inputs: None
  Outputs: Z
  State Variables: A, B, C
Initialization: Reset to (0,0,0)
Equations
  A(t+1) = BC Z = A
  B(t+1) = B’C + BC’= B  C
  C(t+1) = A’C’
Notes: A(t+1) = BC
B(t+1) = B’C + BC’
C(t+1) = A’C’
Z = A

## Slide 66: Step 2: State Table
A B C | A+ B+ C+ | Z
0 0 0 | 0 0 1 | 0
0 0 1 | 0 1 0 | 0
0 1 0 | 0 1 1 | 0
0 1 1 | 1 0 0 | 0
1 0 0 | 0 0 0 | 1
1 0 1 | 0 1 0 | 1
1 1 0 | 0 1 0 | 1
1 1 1 | 1 0 0 | 1
X+ = X(t+1) = Di
  A(t+1) = BC Z = A
  B(t+1) = B’C + BC’ = BC
  C(t+1) = A’C’
Notes: A’B’C’: 0 0 1, 0 1 0, 0 1 1, 1 0 0, 0 0 0, 0 1 0, 0 1 0, 1 0 0
Z: 0 0 0 0 1 1 1 1

## Slide 67: Step 3: State Diagram for the example
Are all states used? Which ones?
A B C | A+B+ C+ | Z
0 0 0 | 0 0 1 | 0
0 0 1 | 0 1 0 | 0
0 1 0 | 0 1 1 | 0
0 1 1 | 1 0 0 | 0
1 0 0 | 0 0 0 | 1
1 0 1 | 0 1 0 | 1
1 1 0 | 0 1 0 | 1
1 1 1 | 1 0 0 | 1
Start from the reset state
000
0
Reset
000
011
010
001
100
101
110
111
Reset
ABC
0
0
0
0
1
1
1
1
Notes: Only states reachable from the reset state 000 are used: 000, 001, 010, 011, and 100.
The circuit produces a 1 on Z after four clock periods and every five clock periods thereafter:
000 -> 001 -> 010 -> 011 -> 100 -> 000 -> 001 -> 010 -> 011 -> 100 …
1 1

## Slide 68: State Diagram
5 states are used: 000, 001, 010, 011, and 100
The function of the circuit
000
011
010
001
100
101
110
111
Reset
ABC
0
0
0
0
1
1
1
1
The circuit produces a 1 on Z after four clock periods and every five clock periods thereafter
Notes: Only states reachable from the reset state 000 are used: 000, 001, 010, 011, and 100.
The circuit produces a 1 on Z after four clock periods and every five clock periods thereafter:
000 -> 001 -> 010 -> 011 -> 100 -> 000 -> 001 -> 010 -> 011 -> 100 …
1 1

## Slide 69: Exercise: State Diagram transitions
A Mealy machine has been implemented with 4 flip-flops, and has 2 inputs (X and Y) and 5 a-synchronous output signals. Consider a complete state diagram for this Mealy machine (i.e. there are no don't cares).
  What is the minimum and maximum number of states?
  What are the minimum and maximum numbers of transition arrows starting at a particular state (leaving the state)?
  What are the minimum and maximum numbers of transition arrows that can end in a particular state?
  What are the minimum and maximum numbers of different binary output patterns that can be observed?

## Slide 70: Exercise: Solution
Number of Inputs, n=2; number of FF, m=4 and number of outputs K=5
In case there are don't cares all states will be used so that the min and max numbers are equal: 24=16.
The number of transitions leaving a state is always 2n = 22 = 4. Thus the max and min is equal to 4.
The number of transitions entering a state: it is possible that non enters a state:
  so that minimum is 0.
  The maximum is when all transitions from all states enter the same state. Thus the maximum will be 2m+n = 26=64.
The max and min. no. of patterns that can be observed at the output:
  Minimum: 1.
  The maximum is either the no. of transitions 2m.2n = 24+2, or 2K = 25, whatever is the smallest. In this case the maximum is thus 25=32.
Notes: Note: for a Moore machine the no. of output patterns is the smallest of: 2m (=no. of states) and 2k.

## Slide 71: 5-5 Sequential Circuit Design
Idea,
New product
Specification
DA
DB
Comb.
Crct.
O
U
T
IN
?
Word description
State Diagram
State Table
Select type of Flip-flop
Input equations to FF, output eq.
Verification
State encoding
Design
procedure

## Slide 72: Specification
Component Forms of Specification
  Written description
  Mathematical description
  Hardware description language
  Tabular description
  Equation description
  Diagram describing operation (not just structure)

## Slide 73: Formulation: Finding a State Diagram
In specifying a circuit, we use states to remember meaningful properties of past input sequences that are essential to predicting future output values.
As an example, a sequence recognizer is a sequential circuit that produces a distinct output value whenever a prescribed pattern of input symbols occur in sequence, i.e, recognizes an input sequence occurrence.
Next, the state diagram, will be converted to a state table from which the circuit will be designed.

## Slide 74: Sequence Detector: 1101
X
CLK
Z
Input X:
Output Z:
00000000001000010010000000100
? Mealy machine
Overlapping sequences are allowed
00111001101011011010011110111
1
1
1
1

## Slide 75: Sequence Detector: 1101
X
CLK
Z
Input X:
Output Z:
00000000001000010010000000100
? Mealy machine
Non-Overlapping sequences are allowed
00111001101011011010011110111
1
1
0
1

## Slide 76: Sequence Detector: 1101
X
CLK
Z
Input X:
Output Z:
00000000001000010010000000100
? Mealy machine
Non-Overlapping sequences are allowed
00111001001010011010011100111
1
1
0
1

## Slide 77: Sequence Detector: 1011
X
CLK
Z
Input X:
Output Z:
00000000001000010010000000100
? Mealy machine
Overlapping sequences are allowed
00111001101011011010011110111
1
1
1
1

## Slide 78: Step 1: Finding a State Diagram
A state is an abstraction of the history of the past applied inputs to the circuit.
  The interpretation of “past inputs” is tied to the synchronous operation of the circuit. E. g., an input value is measured only during the setup-hold time interval for an edge-triggered flip-flop.
  We add states when one needs to remember the past history
Example:
  State A represents the fact that two consecutive 1’s have appeared at the input (i.e. a 1 appears at the input during two consecutive clock edges).
C
In

## Slide 79: State Diagram for the recognizer 1101
Define states for the sequence to be recognized:
  assuming it starts with first symbol X=1,
  continues through the right sequence to be recognized, and
  uses output 1 to mean the full sequence has occurred,
  with output 0 otherwise.
Starting in the initial state (named “S0"):
  Add a state that recognizes the first "1.“
  State “S0" is the initial state, and state “S1" is the state which represents the fact that the "first" one in the input subsequence has occurred. The first “1” occurred while being in state S0 during the clock edge.
S0
S1
1/0
output
input
Reset

## Slide 80: State Diagram for the sequence 1101 (cont.)
Assume that the 2nd 1 arrives of the sequence 1101: needs to be remembered: add a state S2
Next, a “0” arrives: part of the sequence 1101 that needs to be remembered; add state S3
The next input is “1” which is part of the right sequence 1101; now output Z=1
S0
S1
1/0
…1
S2
1/0
…11
0/0
S3
…110
1/1
?

## Slide 81: Completing the state diagram
Where does the final arrow go to:
  The final 1 of the sequence 1101 can be the beginning of another sequence; thus the arrow should go to state S1
?
S0
S1
1/0
…1
S2
1/0
…11
0/0
S3
…110
1/1

## Slide 82: Completing the state diagram
Start is state S0: assume an input X=0 arrives; what is the next state?
Next, consider state S1: input X=0; next state?
Next state S2 and S3: completes the diagram
Each state should have two arrows leaving
S0
S1
1/0
…1
S2
1/0
…11
0/0
S3
…110
1/1
0/0
…0
0/0
0/0
1/0

## Slide 83: Completing the state diagram
Start is state S0: assume an input X=0 arrives; what is the next state?
Next, consider state S1: input X=0; next state?
Next state S2 and S3: completes the diagram
Each state should have two arrows leaving
S0
S1
1/0
…1
S2
1/0
…11
0/0
S3
…110
1/1
0/0
…0
0/0
0/0
1/0

## Slide 84: Step 3: State Assignment
Right now States have names such as S0, S1, S2 and S3
In actuality these state need to be represented by the outputs of the flip-flops.
We need to assign each state to a certain output combination AB of the flip-flops:
  e.g. State S0=00, S1=01, S2=10, S3=11
  Other combinations are possible: S0=00, S1=10, S2=11, S3=01
Combina-tional
Circuit
Storage (D Flip-flops)
External Inputs
State
Next
State
Comb.
crct
CLOCK
Present state
Notes: There are 4x3x2x1=24 possible code assignments, indeed:
For the first one: 4 possibilities: 00, 01, 10, 11
For the 2nd one: 3 possibilities remain,
For the 3rd one: 2 remains.

## Slide 85: Possible state assignments for 4 states with minimum number of bits
For state S0: 4 possibilities (00, 01, 10, 11)
Than for state S1 there will be 3 possible assignments left:
  e.g. is S0=00, then S1 can be 01, 10 and 11
For S2: 2 possible
  e.g. S0=00, S1=01 than S2 can be 10 or 11
For S3: 1 assignment
Thus total of 4x3x2x1=24

## Slide 86: State Assignment – Mealy sequence detector
Popular state assignments:
1. Counting order assignment:
  00, 01, 10, 11
2. Gray code assignment:
  00, 01, 11, 10
3. One-hot state assignment
  0001, 0010, 0100, 1000

## Slide 87: State Assignment: Counting order
“Counting Order” Assignment:
Present State A B | Next State x = 0 x = 1 A+ B+ A+ B+ |  | Output x = 0 x = 1 Z Z | 
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 0 | 0 | 0
1 0 | 1 1 | 1 0 | 0 | 0
1 1 | 0 0 | 0 1 | 0 | 1
Present
State
Next State
x=0 x=1
Output
x=0 x=1
0 0
0 0
0 0
0 1
S0
S0 S1
S1
S0 S2
S2
S3 S2
S3
S0 S1
Resulting coded state table:
S0 = 0 0
S1 = 0 1
S2 = 1 0
S3 = 1 1
State Table:

## Slide 88: State Assignment: Gray code
“Gray Code” Assignment:
Present State A B | Next State x = 0 x = 1 A+ B+ A+ B+ |  | Output x = 0 x = 1 Z Z | 
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 1 | 0 | 0
1 1 | 1 0 | 1 1 | 0 | 0
1 0 | 0 0 | 0 1 | 0 | 1
Present
State
Next State
x=0 x=1
Output
x=0 x=1
0 0
0 0
0 0
0 1
S0
S0 S1
S1
S0 S2
S2
S3 S2
S3
S0 S1
Resulting coded state table:
S0 = 0 0
S1 = 0 1
S2 = 1 1
S3 = 1 0
State Table:

## Slide 89: Step 4: Find Flip-Flop Input and Output Equations
Idea,
New product
Specification
DA
DB
Comb.
Crct.
O
U
T
IN
State Diagram
State Table
Select type of Flip-flop
Input equations to FF, output eq.
Verification
State encoding
A
B
Next state A+ and B+

## Slide 90: Find Flip-Flop Input and Output Equations: Example – Counting Order Assignment
1
0
0
0
0
0
1
1
Using D flip-flops: thus DA=A+, DB=B+(the state table is the truth table for DA and DB).
Interchange the bottom two rows of the state table, to obtain K-maps for DA, DB, and Z:
Present State | Next State x = 0 x = 1 |  | Output x = 0 x = 1 | 
AB | A+ B+ | A+ B+ | Z | Z
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 0 | 0 | 0
1 0 | 1 1 | 1 0 | 0 | 0
1 1 | 0 0 | 0 1 | 0 | 1
DA = AB + XAB
DB = XAB + XAB + XAB
Z = XAB
Gate Input Cost = 22
(plus FF: each FF needs about 14 gate inputs)
B
A
X
DA
0
0
1
0
1
0
0
1
B
A
X
DB
Notes: Input gate cost: DA: 7
DB: 12
Output 3
Total is 22 not counting inverters

## Slide 91: Find Flip-Flop Input and Output Equations: – Gray Code Assignment
Assume D flip-flops
K-maps:
B
A
X
1
0
1
0
1
0
1
0
B
A
X
0
0
0
0
1
1
1
0
DA
DB
Present State A B | Next State x = 0 x = 1 A+ B+ A+ B+ |  | Output x = 0 x = 1 Z Z | 
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 1 | 0 | 0
1 1 | 1 0 | 1 1 | 0 | 1
1 0 | 0 0 | 0 1 | 0 | 0
DA = AB + XB
DB = X
Gate Input Cost = 9
Z = XAB’

## Slide 92: Circuit for Gray Code assignment: Map Technology
DA = AB + XB
DB = X
Z = XAB’
5V
DA
DB
A
B
Clock
D
D
C
R
Z
C
R
X
Reset
Reset

## Slide 93: Exercise: Map the Circuit into Nand-Nand implementation
DA = AB + XB
DB = X
Z = XAB’
5V
DA
DB
A
B
Clock
D
D
C
R
Z
C
R
X
Reset
Reset
Z

## Slide 94: Alternative State Assignment: One FF per state
One Flip-flop per State or One-Hot Assignment
Example codes for four states:
Now requires 4 flip-flops:
S3, S2, S1, S0 = 0001, 0010, 0100, and 1000.

## Slide 95: One-hot State Assignment – Previous example
One-Hot Assignment:
Present State ABCD | Next State x = 0 x = 1 A+B+C+D+ |  | Output x = 0 x = 1 | 
S0 1000 | 1000 | 0100 | 0 | 0
S1 0100 | 1000 | 0010 | 0 | 0
S2 0010 | 0001 | 0010 | 0 | 0
S3 0001 | 1000 | 0100 | 0 | 1
Present
State
Next State
x=0 x=1
Output
x=0 x=1
0 0
0 0
0 0
0 1
S0
S0 S1
S1
S0 S2
S2
S3 S2
S3
S0 S1
S0 = 1000
S1 = 0100
S2 = 0010
S3 = 0001
State Table:

## Slide 96: Optimization: One Hot Assignment
Equations can be easily determined from the table:
A+ = DA = X(S0+ S1 + S3)=X(A+B+D)
B+ = DB = X(S0+ S3)= X(A+D)
C+ = DC = X(S1+ S2)=X(B+C)
D+ = DD = X S2 = X C
Z = XS3 = X D
Gate Input Cost = 17
Combinational cost intermediate plus cost of two more flip-flops needed.
Advantages: ease of design, reliability and performance
Present State ABCD | Next State x = 0 x = 1 A+B+C+D+ |  | Output Z x = 0 x = 1 | 
S0 1000 | 1000 | 0100 | 0 | 0
S1 0100 | 1000 | 0010 | 0 | 0
S2 0010 | 0001 | 0010 | 0 | 0
S3 0001 | 1000 | 0100 | 0 | 1
In equations, only the variable that is 1 for the state needs to be included, e. g., state with code 0001, is represented in equations by S0 instead of S3 S2 S1 S0 because all codes with 0 or two or more 1s have don’t care next state values.

## Slide 97: Circuit for the One-Hot coded circuit
DA = X(A+B+D)
DB = X(A+D)
DC = X(B+C)
DD = X C
Z = X D
5V

## Slide 98: Example: Vending machine
Design the control circuit for a vending machine with the following specifications:
    The vending machine accepts nickels (N) and dimes (D)
    When the machine has received 15 cents it delivers a package of candy.
    If too much money has been added, the machine returns the difference.
    When the candy has been released, ,the release mechanism brings the circuit back to the original, starting state.
Coin
insert
release

## Slide 99: Design Procedure - review
Understanding the problem and adding specs if needed
State diagram
State table
State encoding
Select the type of flip-flop
Derive the input equations to the FF; and the output equations
Draw the diagram
Verify

## Slide 100: Step 1: Understanding the problem
Only one of the inputs N or D are asserted at one time (never together)
N and D is asserted for only one clock cycle when a coin has been inserted
Pennies are not accepted
Z=0 (no change); Z=1 (change returned: 5 cents)
Coin
sensor
N
D
Release candy
mechanism
Return change
mechanism
Y
Z
Inputs: N and D
Outputs: Y and Z
Vending
Sequential Crt

## Slide 101: Step 2: State Diagram (Moore)
Si
YZ
ND
S0
00
Reset
S1
00
Convention:
output
input
state
N
S3
10
N
5c
S2
00
N
10c
15c
release
gum
X
D
D
S4
11
D
20c
release gum;
return 5c
X
Requires 5 states

## Slide 102: Step 2: State Diagram (Mealy)
Si
ND/YZ
S0
Reset
Convention:
output
Input/
state
N/00
S1
5c
S2
N/00
10c
Requires 3 states
D/00
20c
release gum;
return 5c
D/11
D/10
15c
release
gum
N/10

## Slide 103: Step 2: State Diagram (Mealy)
Si
ND/YZ
S0
Reset
Convention:
output
Input/
state
N/00
S1
5c
S2
N/00
10c
D/00
20c
release gum;
return 5c
D/11
D/10
15c
release
gum
N/10
The notation in the previous diagram was simplified: we assumed that when an input=0 there is no change.
A more complete diagram would be:
N.D
N.D
N.D

## Slide 104: Step 3: State table for Mealy machine
Present State | Inputs D N | Next States | Outputs Y Z
S0 | 0 0 | S0 | 0 0
S0 | 0 1 | S1 | 0 0
S0 | 1 0 | S2 | 0 0
S0 | 1 1 | x | x x
S1 | 0 0 | S1 | 0 0
S1 | 0 1 | S2 | 0 0
S1 | 1 0 | S0 | 1 0
S1 | 1 1 | x | x x
S2 | 0 0 | S2 | 0 0
S2 | 0 1 | S0 | 1 0
S2 | 1 0 | S0 | 1 1
S2 | 1 1 | x | x x
S3 | 0 0 | x | x x
S3 | 0 1 | x | x x
S3 | 1 0 | x | x x
S3 | 1 1 | x | x x
S0
Reset
N/00
S1
5c
S2
N/00
10c
D/00
D/11
D/10
N/10

## Slide 105: Step 4: State Encoding
Three states requires 2 flip-flops: A and B
Use the following encoding:
  S0 = 00
  S1 = 01
  S2 = 10
Encoded state table

## Slide 106: Encoded state table
Present State | Inputs D N | Next States | Outputs Y Z
S0 | 0 0 | S0 | 0 0
S0 | 0 1 | S1 | 0 0
S0 | 1 0 | S2 | 0 0
S0 | 1 1 | x | x x
S1 | 0 0 | S1 | 0 0
S1 | 0 1 | S2 | 0 0
S1 | 1 0 | S0 | 1 0
S1 | 1 1 | x | x x
S2 | 0 0 | S2 | 0 0
S2 | 0 1 | S0 | 1 0
S2 | 1 0 | S0 | 1 1
S2 | 1 1 | x | x x
S3 | 0 0 | x | x x
S3 | 0 1 | x | x x
S3 | 1 0 | x | x x
S3 | 1 1 | x | x x
Present State A B | Inputs D N | Next States A+ B+ | Outputs Y Z
0 0 | 0 0 | 0 0 | 0 0
0 0 | 0 1 | 0 1 | 0 0
0 0 | 1 0 | 1 0 | 0 0
0 0 | 1 1 | x | x x
0 1 | 0 0 | 0 1 | 0 0
0 1 | 0 1 | 1 0 | 0 0
0 1 | 1 0 | 0 0 | 1 0
0 1 | 1 1 | x | x x
1 0 | 0 0 | 1 0 | 0 0
1 0 | 0 1 | 0 0 | 1 0
1 0 | 1 0 | 0 0 | 1 1
1 0 | 1 1 | x | x x
1 1 | 0 0 | x | x x
1 1 | 0 1 | x | x x
1 1 | 1 0 | x | x x
1 1 | 1 1 | x | x x

## Slide 107: Step 5: Select type of flip-flop
We will use D flip-flops: A and B
Other flip-flops are possible (see later):
  JK flip-flop
  SR flip-flop
  T flip-flop

## Slide 108: Step 6: Derive the inputs to the flip-flops and output equations
The combinational circuits can be implemented in a variety of ways:
  Minimized SOP
  Decoders and OR gates
  Multiplexers
Let’s use the minimized SOP:
  Use K-maps for optimization

## Slide 109: Input equations for DA and DB
Present State A B | Inputs D N | Next States A+ B+ | Outputs Y Z
0 0 | 0 0 | 0 0 | 0 0
0 0 | 0 1 | 0 1 | 0 0
0 0 | 1 0 | 1 0 | 0 0
0 0 | 1 1 | x | x x
0 1 | 0 0 | 0 1 | 0 0
0 1 | 0 1 | 1 0 | 0 0
0 1 | 1 0 | 0 0 | 1 0
0 1 | 1 1 | x | x x
1 0 | 0 0 | 1 0 | 0 0
1 0 | 0 1 | 0 0 | 1 0
1 0 | 1 0 | 0 0 | 1 1
1 0 | 1 1 | x | x x
1 1 | 0 0 | x | x x
1 1 | 0 1 | x | x x
1 1 | 1 0 | x | x x
1 1 | 1 1 | x | x x
0
x
0
1
1
0
B
D
N
A
1
x
x
x
x
DA
0
x
x
0
0
0
x
0
0
0
0
B
D
N
A
0
x
x
x
x
DB
1
x
x
1
0
DA=BN+ABD+AND
DB=BND+ABN

## Slide 110: Output equations
Present State A B | Inputs N D | Next States A+ B+ | Outputs Y Z
0 0 | 0 0 | 0 0 | 0 0
0 0 | 0 1 | 0 1 | 0 0
0 0 | 1 0 | 1 0 | 0 0
0 0 | 1 1 | x | x x
0 1 | 0 0 | 0 1 | 0 0
0 1 | 0 1 | 1 0 | 0 0
0 1 | 1 0 | 0 0 | 1 0
0 1 | 1 1 | x | x x
1 0 | 0 0 | 1 0 | 0 0
1 0 | 0 1 | 0 0 | 1 0
1 0 | 1 0 | 0 0 | 1 1
1 0 | 1 1 | x | x x
1 1 | 0 0 | x | x x
1 1 | 0 1 | x | x x
1 1 | 1 0 | x | x x
1 1 | 1 1 | x | x x
1
x
0
0
0
1
B
D
N
A
0
x
x
x
x
Y
0
x
x
0
1
0
x
0
0
0
1
B
D
N
A
0
x
x
x
x
Z
0
x
x
0
0
Y=BD+AN+AD
Z=AD

## Slide 111: Step 7: Circuit
D
Q
DA
A
D
Q
DB
B
DA=BN+ABD+AND
DB=BND+ABN
Y=BD+AN+AD
Z=AD
D
N
Y
Z
CLK

## Slide 112: Simulation and verification: Mealy machine
N
N
N
release
N
D
release
D
D
glitches
Release &
Change (OK)
wrong output
glitch
inputs
outputs
Y
Z

## Slide 113: Mealy machine: extra outputs!
Did anything go wrong?
Key: when is the input valid?
  A set-up time before the clock transition: in our case this is just before the positive clock edge:
  Thus, the output is valid just before the clock edge (i.e. at the end of the state time): for state Si and valid input In
tS
th
In
valid In
Clock
State Si+1
State Si
Out
Valid
Not necessarily valid
Si
In/out
Si
In/out

## Slide 114: Mealy machine: simulation
Output are only valid at the end of the state time!
Be careful with outputs of Mealy machines.

## Slide 115: Moore machine: timing
Since the output is only function of the state and NOT of the inputs: timing is easier.
The output is valid at the next clock cycle (when in the new state Si+1)
Clock
State Si+1
State Si
Out
tS
th
In
valid In
Valid
in
Si
Outi
Si+1
Outi+1
Outi
Outi+1

## Slide 117: Step 8: Simulation and verification: Moore machine
N
N
N
release
N
D
release
D
D
Release &
Change (OK)
Moore machine gives the correct outputs

## Slide 118: 5-6 Other Flip-Flop Types
J-K and T flip-flops
  Behavior
  Implementation
Basic descriptors for understanding and using different flip-flop types
  Characteristic tables
  Characteristic equations
  Excitation tables

## Slide 119: J-K Flip-flop
Behavior of JK flip-flop:
  Same as S-R flip-flop with J analogous to S and K analogous to R
  Except that J = K = 1 is allowed, and
  For J = K = 1, the flip-flop changes to the opposite state (toggle)
Behavior described by the characteristic table (function table):
J
C
K
Q
J K Q(t+1)
0 0 Q(t) no change
0 1 0 reset
0 1 set
1 1 Q(t) toggle

## Slide 120: Design of a J-K Flip-Flop
State table of a JK FF:
Q J K Q(t+1)
Present Inputs Next
state state
0
0
1
1
1
0
1
0
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
Q
J
K
Q(t+1)=DA
0 0 1 1
1 0 0 1
Q(t+1)= DA=JQ’ + K’Q
Called the characteristic equation
D
C
K
J

## Slide 121: T Flip-flop
Behavior described by its characteristic table:
  Has a single input T
    For T = 0, no change to state
    For T = 1, changes to opposite state
Characteristic equation:
Q(t+1)=T’Q(t) + TQ’(t)
= TQ(t)
T
C
T Q(t+1)
0 Q(t) no change
1 Q(t) complement

## Slide 122: T Flip-flop realization
Using a D Flip-flop: D=TQ(t)
Or use a J-K flip-flop:
C
D
T
J K Q(t+1)
0 0 Q(t)
0 1 0
0 1
1 1 Q’(t)
Make J=K=T

## Slide 123: Excitation table of Flip-Flops
  Characteristic table - defines the next state of the flip-flop in terms of flip-flop inputs and current state
  Characteristic equation - defines the next state of the flip-flop as a Boolean function of the flip-flop inputs and the current state.
  Excitation table - defines the flip-flop input variable values as function of the current state and next state. In other words, the table tells us what input is needed to cause a transition from the current state to a specific next state.
For analysis
For design